## Slide 1: Ergonomics Process Training for Grocery Workers
Notes: This training is designed for use with safety committees, management, or those who need more advanced ergonomics training.
Total training time: 4 – 6 hours.
  Training sessions can be split at each “stop sign” or anywhere there is a title slide, such as the ‘What is Ergonomics?’ slide.
  The section on common work-related musculoskeletal disorders is optional. This includes the slides on low back disorders, carpal tunnel syndrome, and rotator cuff injury.
This training program should be supplemented with video clips of workers performing grocery tasks in your store(s). These videos can be used to practice:
  Identification of risk factors and possible MSDs that could result from the tasks
  Use of ergonomic exposure assessment methods to quantify risk factors
  Development of ergonomic solutions to reduce exposure to these risk factors

## Slide 2: Outline
Introduction to Ergonomics
Hazards of Ignoring Ergonomics
Implementing Ergonomics and Solutions
The Ergonomics Process
Ergonomic Problem Solving
Notes: This is a ‘crash course’ in ergonomics for grocery workers
The purpose is for you to become familiar in basic ergonomic principles, musculoskeletal disorders (MSDs) and associated risk factors, solutions or controls to reduce exposure to these risk factors, and the Ergonomic Process used to implement controls.

## Slide 3: Outline
Introduction to Ergonomics
  What is ergonomics and why do ergonomics?
  Modifiable grocery workplace factors
Hazards of Ignoring Ergonomics
Implementing Ergonomics and Solutions
The Ergonomics Process
Ergonomic Problem Solving

## Slide 4: What is Ergonomics?
Notes: Ask participants, “what is ergonomics?”
Give participants a chance to respond. If no response, possible follow-up questions:
  Anybody have a computer? What problem are you supposed to get from using a keyboard?
  Anybody lift anything this past weekend? How are you supposed to lift?
Emphasize that ergonomics is more than keyboards and proper lifting techniques.

## Slide 5
Ergonomics
“designing the job to fit the worker”
Notes: Give this simple, applied definition
Emphasize that most workers have to fit to the job rather than the other way around.

## Slide 6
Ergonomics
“there’s gotta be an easier way”
Notes: Here’s an even more applied definition
You are thinking like an ergonomist if you find an easier way to do something.
Give example, such as if you have to lift 50 lb bag, ask yourself “is there an easier way to do this?”

## Slide 7: Why do Ergonomics?

## Slide 8: Why Do Ergonomics?
Prevent injuries & illnesses
Efficient production
Product quality
Quality of work life
Goals
Notes: What are the goals of ergonomics? Why pay attention to ergonomics?
  Prevent injuries & illnesses: the most common injuries/illnesses influenced by ergonomics are called “musculoskeletal disorders” (MSD).
    The injury is to the musculoskeletal system and could include muscles, bones, joints, ligaments and/or nerves.
  Efficient production: How does good ergonomics improve production or product quality?”
  Product quality: What is the ‘product’ in a grocery store? (food, customer service).
    Consider how a worker with a painful back might handle heavy product. Is there a chance that product may be damaged by workers dropping it because their back hurts?
  Quality of work life: Emphasize quality of work life such as “no one wants to go home at the end of the day feeling worse than we did when we first started work. You want to go home without a back or knee injury.”

## Slide 9: Why Do Ergonomics? Health & Safety Practitioners
Physical discomfort
Physical fatigue
Mental stress
Injuries and illnesses
Cost of medical treatment
Notes: Why are health and safety practitioners (such as safety managers) interested in ergonomics?
Briefly discuss each concept and how ergonomics could affect each

## Slide 10: Why Do Ergonomics? Company
Efficient production methods
Reduce waste
Product quality
Total quality management (TQM)
Notes: Why would your company be interested in ergonomics?
Briefly discuss each concept and how ergonomics could affect each
Total quality management was coined by Dr. W. Edwards Deming (1900-1993). It is a method of continuous improvement in the quality of products, services, and people. Similar concepts used in manufacturing environments are Lean Manufacturing and Six Sigma.
  The Ergonomics Process described later is similar to TQM

## Slide 11: Why Do Ergonomics? USA Standards
Occupational Safety and Health Act of 1970
  General Duty Clause
“Each employer shall furnish to each of his employees, employment and a place of employment which is free from recognized hazards that are causing of are likely to cause death or serious harm to his employees.”
Notes: Are there any federal government regulations about ergonomics?
  Ergonomic issues are addressed in the “General Duty Clause.”
What is the Occupational Safety and Health Act of 1970? (OSHA)
The whole point of the General Duty Clause is to try to keep risks to a minimum.
Emphasize that it's almost impossible for work to be completely risk free.

## Slide 12: Why Do Ergonomics? State of Washington Standards
Safe Place requirement
  WAC 296-800-110
  Washington’s version of the General Duty Clause
Employers are responsible for providing “a safe and healthy workplace free from recognized hazards.”
Notes: The Department of Occupational Safety and Health (DOSH) is the State of Washington’s version of OSHA
Washington employers follow DOSH rules, not OSHA rules, such as the Safe Place requirement.
URL to the Safe Place requirements: http://www.lni.wa.gov/wisha/rules/corerules/PDFs/296-800-110.pdf

## Slide 13: Modifiable Grocery Workplace Factors
Notes: Now we will talk about factors that can be modified to make the grocery workplace more ‘ergonomic.’

## Slide 14: Workspace
Notes: What do you think of the workspace you are sitting at right now (e.g., tables and chairs)?
Why are the tables and chairs at this height?
  Fits the “average” person.
  Follow up question, “Who is the average person?” Emphasize that designing for the average person means only a few people may fit comfortably.

## Slide 15: Workspace
Reaching out
Reaching up
Work surface height
Leg room
Twisting
Upper body posture
Notes: Workspace has to do with things like:
  Reaching out and reaching up.
    Examples: depth of shelves, storeroom, bins for produce, display case in deli.
    Have the tallest and shortest persons in the audience demonstrate the differences in their reach in these directions.
  Work surface height.
    Examples: shelf height, tables in meat and bakery departments
    Emphasize that the floor is often the work height in grocery stores.
    What do you think of the work surface where you are currently sitting? (Discuss who it fits and who it doesn’t. Discuss why the surface is that height {average person} and then decide who is “average” {nobody for all workspace parameters})
  Legroom.
    Mainly related to sitting.
    What do you think of the legroom where you are currently sitting?
  Twisting.
    Ask what’s wrong with twisting and if there are tasks that workers must twist.
  Upper body posture.
    Examples: reaching out or overhead.

## Slide 16
Notes: Have participants look at this workspace and refer back to previous slide.
  You will first look at some workers doing jobs other than grocery tasks. This will help you develop a good eye for ergonomics.
  This person is assembling circuit boards and has to reach frequently to get certain parts.
  What are some good things about this workspace?
    Parts are close so possibly minimal horizontal/vertical reach.
    Work surface height appropriate for task.
    Good leg room.
    No twisting needed.
    Parts appear light.
  What are some bad things about this workspace?
    Horizontal reach could be bad if he has to do this frequently.
    Upper body posture requires reach.

## Slide 17
Notes: Have participants look at this workspace.
  What are some good things about this workspace?
    Minimal horizontal reach.
    Work surface height appropriate for task.
  What are some bad things about this workspace?
    Possible excessive vertical reach.
    Possible twisting to put meat on rack.

## Slide 18: Work Posture

## Slide 19: Work Posture
Bending
Crouching
Head and neck angle
Shoulder-arm angle
Hand & wrist angle
Static holding
Notes: Work posture has to do with:
  Bending forward or backward at the waist
  Crouching or squatting
  How far the head is bent forward on the neck
  How high the arms are raised
  If the wrist is excessively bent forward or backward
  Static holding or keeping a body part in a certain position for a long period of time
    Most often has to do with the neck being bent forward.

## Slide 20
Notes: Worker is reaching into the deli case
  What are some good things about this work posture?
    None
  What are some bad things about this work posture?
    Bending
    Shoulder-arm angle at 90° (find out later why this is a problem)
    Head-neck angle poor because of case top
Have participants work together to come up with ideas to improve work posture.
Give a handout of brainstorming rules at this point.
  Everyone takes a turn
  Have several ideas
  Think out of the box
  Don’t criticize other’s ideas
  List ideas on flipchart or whiteboard without editing
  Do not modify any ideas until all are listed

## Slide 21: Manual Materials Handling
Notes: Manual material handling is probably the most common ergonomic factor in grocery stores.
  Lifting
  Carrying
  Pushing
  Pulling

## Slide 22: Manual Materials Handling
Lifting, carrying, pushing, and pulling
  Weight
  Size
  Handgrips
  Starting and ending points
  Twisting and upper body movements
  Frequency and duration
  Footing and tight spaces
Notes: These are all issues to consider when talking about MMH, whether it involves lifting, carrying, pushing, or pulling:
  Weight of the product is a key factor to consider. NIOSH suggests that any lift over 51 lb could be hazardous.
  Size: in general, the larger the object to be moved, the more risk it poses.
  Are there handgrips on all the boxes? (No, most of them don't have handgrips). Handgrips allow easier handling.
  Starting and ending points: Are workers lifting from the floor or above shoulder level?
  Do you have to twist? What is your upper body doing?
  Frequency and duration: how often do you lift and what percentage of the day requires MMH tasks?
  What about tight spaces (also called “confined spaces”)? Consider the store room during Thanksgiving.

## Slide 23
Notes: Ask about the following factors:
  Weight: dough ~115 lb. if lifted at one time.
  Size: big and bulky
  Handgrips: none
  Starting and ending points: mixing bowl (between the knees) to table height
  Twisting and upper body movements?
  Frequency and duration
  Footing and confined spaces
Do you think this is a hazardous lift?
  If so, what can be done about it?

## Slide 24
Notes: Ask about the following factors:
  Weight: dog food ~35 lb.
  Size: big and bulky
  Handgrips: none
  Starting and ending points: pallet (close to floor) to above shoulders
  Twisting and upper body movements?
  Frequency and duration
  Footing and confined spaces
Do you think this is a hazardous lift?
  If so, what can be done about it?

## Slide 25: Gripping
Notes: How we grasp objects during the day is another factor that can be changed.

## Slide 26: Gripping
Wrist posture
Forceful exertions
Grip dimensions
Repetition rate
Static holding
Notes: Factors related to gripping include:
  Wrist posture: is the wrist in neutral or bent forward/backward?
    Talk about “neutral” joint positions here. Neutral is around the natural resting position of the joint with the wrist straight like shaking someone’s hand.
      Working in neutral joint position helps lessen the stress on muscles, tendons, and ligaments around a joint.
  Do workers have to forcefully grip objects?
    Examples: meat cutting, deli, cutting produce
  How wide or narrow is the grip workers have to use?
    Examples: meat cutting, deli, cutting produce
  Repetition has to do with how frequently workers have to grip
    Examples: checkout
  Static holding has to do with holding an object in one place while doing something like cutting
    Examples: meat and fish department
    Ask why static holding is not good if done repetitively (decreased blood flow).

## Slide 27
Notes: This worker is rolling out dough.
Would this type of gripping be easy or difficult?
  Wrist posture: wrist is bent back which could be a risk factor for wrist tendonitis.
  Forceful exertions: possibly depending on the thickness of the dough.
  Grip dimensions: small in this case.
  Repetition rate: high repetition.
  Static holding: possibly depending on how long her hands are in contact with the dough.

## Slide 28: Tools
Notes: Are any hand tools used in the grocery store?
  Examples: box knife, knives in the meat department or deli, scissors in floral department, pallet jacks

## Slide 29: Tools
Grip size, span, shape
Wrist angle
Weight and balance
Pressure
Maneuverability
Vibration
Notes: Regardless of the tool, consider these factors:
  The tool grip size, span, and shape of the handle.
    Who are these tools usually designed for? (males)
  Is the wrist positioned in neutral while using the tool?
  How heavy is the tool and is it easy to hold?
  Does the tool require a lot of contact pressure with the handle?
  Is the tool easy to maneuver?
  Is there any vibration associated with the hand tools?
    Example: floor scrubbers

## Slide 30
Notes: VIDEO: tools – remove fat.mp4/wmv
Consider these factors with this video of a meat cutter removing fat):
  Grip size, span, shape: good design
  Wrist angle: depends on the worker’s ability to maneuver the meat.
  Weight and balance: lightweight.
  Pressure: minimal.
  Maneuverability: easy.
  Vibration: may be an issue if used for prolonged durations.

## Slide 31
Notes: VIDEO: tools – pallet jack.mp4/wmv
Consider these factors with a pallet jack:
  Grip size, span, shape: easy to grip the handle.
  Wrist angle: often requires the wrist to bend when first moving pallets.
  Weight: potentially heavy, especially when first moving pallets.
  Pressure: minimal.
  Maneuverability: ask what factors could affect the ability to move pallets?
    Examples: maintenance of smooth rolling wheels, where the truck drive places pallets when unloading truck.
  Vibration: not an issue.
Note that the video shows how workers will use a tool in a way it is not designed to accomplish their task. One fork was used to move the pallet because someone placed the pallet incorrectly.

## Slide 32: Store Organization
Layout of materials
Machine pacing
Work-rest schedule
Notes: Store organization factors include:
  Layout: how organized are the storerooms? Are items handled more than necessary?
  Machine pacing: this is when a machine determines the pace of work, rather than the worker.
    Assembly lines are a good example of machine pacing.
    What are examples of machine pacing in grocery stores? (grinding hamburger, meat wrapping machines, and possibly cutting meats in the deli).
  Work-rest schedule: do workers have the ability to take “mini-breaks?”
    Examples: alternate between heavy and light lifting; if reaching overhead a lot, can you do some work in front.

## Slide 33
Notes: The next 3 slides are an example of poor work organization from a factory.
This worker takes a part weighting about 80 lb off the line and has to walk over to a pallet.

## Slide 34
Notes:   He then places the part into a pallet box.

## Slide 35
Notes: About 20 yards away, someone takes it out of the same box.
  So, the part is handled twice when it could possibly be handled only once
Are there any examples of this type of work organization in the grocery store? (double or triple handling of a product)

## Slide 36
Notes: What do you think about the layout of this freezer?
Are there any solutions?

## Slide 37: Environment
Notes: Environmental factors also have an affect on ergonomics

## Slide 38: Environment
Temperature
Humidity
Clothing (gloves)
Illumination
Noise
Notes: Issues related to environment include:
  Temperature: generally comfortable except for extended work in the freezer or work outside.
  Humidity: the higher the humidity, the greater the physiological impact.
  Clothing: if warmer clothing is worn (meat department), does it interfere with movement? Gloves help to protect the hands but require a more forceful grip.
  Illumination: are there parts of the storeroom where lighting is poor?
  Noise: are there any locations of a grocery store that are excessively noisy? (trash compactor, meat wrapping machines).
    If workers stay in these locations for a long period of time, ear plugs might be important to use.

## Slide 39
Notes: Next we will talk about the hazards of ignoring ergonomics.
This is a good time for a break.
  Encourage participants to stand up and walk around during break.

## Slide 40: Outline
Introduction to Ergonomics
Hazards of Ignoring Ergonomics
  Risk factors
  Direct and indirect costs
    Work-related musculoskeletal disorders
Implementing Ergonomics and Solutions
The Ergonomics Process
Ergonomic Problem Solving
Notes: Introduce the next section by emphasizing that risk factors are probably one of the most important concepts to understand about ergonomics
implementation

## Slide 41: Risk Factors that Could Cause Occupational Injury
Notes: There are certain risk factors that we know are related to occupational injury.
For example, it is well established that heavy lifting is associated with low back disorders.

## Slide 42: Risk Factors in the Grocery Store
Heavy lifting
Awkward postures
Static postures
High repetition
Forceful hand exertions
Hand-arm vibration
Personal factors
Notes: These are the primary risk factors that affect grocery workers:
  Heavy lifting
  Awkward postures of any joint (such as the wrists, shoulders, or back)
  Static postures or staying in one position for a long period of time
  Forceful gripping
  Highly repetitive hand movements
  Vibration of the hand (there is also whole-body vibration but this risk factor is uncommon in grocery stores)
  Personal factors
We will review each of these.

## Slide 43: Risk Factors: Heavy Lifting
Notes: VIDEO: lifting – flour bag BL.mp4/wmv
These workers are unloading bags of flour weighing about 50 lbs.
Heavy lifting is a risk factor associated with low back and shoulder injuries.
Review the factors related to MMH for this task:
  Weight of the flour is around 50 lbs. so it could be considered hazardous.
  Size: not unreasonable
  Handgrips: none so the worker has to exert more to lift
  Starting and ending points: lifts originate anywhere from knee height (OK) to cart height (poor).
  Twisting: possible due to position of cart in relation to the end point.
  Frequency and duration: only done once or twice a day so good.
  Tight spaces: many bakeries have limited room to maneuver.
Are there any solutions to make this job easier on the low back? (scissors lift pallet jack, keep bags on original pallet to avoid double handling)
  This is a good time to introduce the concept of ergonomic solutions as ways to minimize or remove risk factors.

## Slide 44: Risk Factors: Heavy Lifting
Notes: VIDEO: lifting – dog food overhead BL.mp4/wmv
This worker is lifting bags of dog food weighing up to 35 lb. from the pallet to the top shelf.
Note the age of this worker.
  Could someone older do this task?
  Could someone with shoulder or back pain do this task?
  Could all your customers lift product from the top or bottom shelves?
Review the factors related to MMH for this task:
  Weight of the dog food is under 55 lb. so not considered hazardous for this factor.
  Size: not unreasonable
  Handgrips: none so the worker has to exert more to lift
  Starting and ending points: lifts originate anywhere from knee height (OK) to pallet height (poor).
  Twisting: likely
  Frequency and duration: only done once a day although entire pallet may be unloaded.
  Confined spaces: none.
Are there any solutions to make this job easier on the shoulders? (position heavier bags of dog food between knee and chest height, lift teams, raise the pallet with scissors lift pallet jack)

## Slide 45: Risk Factors: Heavy Lifting
Notes: Lets return to the person lifting dough. Would this weight (~115 lb) be considered too much to lift all at once? (yes)
Is there a way to safely lift this weight alone? (no)
Other than weight of the dough, what are some things that makes this lift hazardous? Have participants return to the slide on Manual Material Handling for ideas (no real handgrip, size of dough).

## Slide 46
Notes: This is a biomechanical model of the same lift.
Lifts that put the upper bar in the red zone are clearly hazardous.
The biomechanical model suggests that the worker would put over 1600 lb of compression force on his low back while lifting dough.
  Compression forces greater than 770 lb. are hazardous.
How could this lifting task be easier? (cut small sections of dough instead of lifting all at once, bowl lift).
  Lift teams are sometimes a good solution for heavy lifting but would not be effective in this case.

## Slide 47: Risk Factors: Awkward Postures
Stooped postures
Notes: VIDEO: awkward back posture - grinding hamburger BL.mp4/wmv
This worker is grinding meat for hamburger in a stooped posture.
What part of the body is in an awkward posture? (low back)
A posture can be considered awkward when the joint is being used at the extremes of range of motion. This risk factor is associated with various MSDs, depending on the joint.
Are there any solutions to make this job easier on the low back? (lift for bowl, lift smaller portions as she does, intermittently squat [but hard on knees])

## Slide 48: Risk Factors: Awkward Postures
“Chicken wings”
Notes: VIDEO: awkward shoulder posture - chicken wings flour BL.mp4/wmv
This worker is measuring flour into a mixing bowl.
What part of the body is in an awkward posture? (left shoulder)
  This is called a “chicken wings” posture.
  ACTIVITY: Have participants place an arm to their side with their thumb down and then attempt to raise their arm overhead. Notice how difficult it is. Then have them raise the same arm with the thumb up and notice how they can raise arms higher. The first position is “chicken wings” and is hard on the shoulder, possibly leading to rotator cuff injury.
What is a common injury among baseball pitchers? (rotator cuff tears)
  The end of the pitching motion is a chicken wing position.
  Getting in this position one time will not cause a rotator cuff injury; repetitive awkward postures are the problem.
Are there any solutions to make this job easier on the shoulder? (lower the bowl, pour flour in at one time)

## Slide 49: Risk Factors: Static Posture
Notes: VIDEO: static posture neck - meat cutting BL.mp4/wmv
Static postures are when a joint is held in an awkward position for long durations. These postures can lead to various MSDs of the neck and low back.
What part of the body is in a static posture? (neck)
  How heavy does your head weigh? (about 10 – 15 lbs)
    ACTIVITY: Have a bowling ball or 10 lb. weight available. Have a participant hold the ball/weight for 30 seconds with one hand and their forearm vertical. Next, have the participant hold the ball/weight for 30 seconds (if possible) with one hand and their forearm about 6 inches away from vertical. Ask participant where they feel tension (usually the forearm or biceps). Relate this tension to the tension in the shoulder/upper back with a static forward head posture.
Are there any solutions to make this job easier on the neck and get the neck out of a static posture?
  Raise the work surface (but this could bring the shoulders into an awkward posture).
  Place frequently used items higher so the worker has to look up and reach to retrieve them.

## Slide 50: Risk Factors: High Repetition
Notes: VIDEO: repetition – cashiering BL.mp4/wmv
Highly repetitive tasks also affect the hand, wrist, and elbow. They can lead to MSDs of the hand, wrist, and elbow such as elbow tendonitis (tennis elbow), carpal tunnel syndrome, and finger tendonitis.
Repetition is considered high if the job cycle is less than 30 seconds. The job cycle is when one object is the time between one object being picked up and the next one.
  This task is considered high repetition.
Are there any solutions to make this job easier on the hands?
  Job rotation to other checkout stands or other tasks.

## Slide 51: Risk Factors: Forceful Hand Exertions
Notes: VIDEO: forceful hand exertions - fill Jelly doughnut BL.mp4/wmv
This worker is filling jelly doughnuts by squeezing a pastry bag. Depending on the consistency of the contents, the task can require significant hand exertion.
Forceful hand exertions are those requiring substantial gripping. They often occur with awkward postures of the wrist and repetitive hand movements. Forceful exertions can lead to MSDs of the hand, wrist, and elbow such as elbow tendonitis (tennis elbow), carpal tunnel syndrome, and finger tendonitis
Are there any solutions to make this job easier on the hands?

## Slide 52: Risk Factors: Hand-Arm Vibration
Notes: Exposure to hand-arm vibration (HAV) is not common in grocery stores except for the custodians who use floor scrubbers/polishers. We usually think of this risk factor when using tools such as chain saws or jackhammers.
Prolonged exposure to vibrating tools can lead to MSDs of the hand, wrist, and elbow such as elbow tendonitis (tennis elbow), carpal tunnel syndrome, and finger tendonitis.
  Tendonitis can occur because we automatically grip tighter whenever we grasp a vibrating tools.
  Carpal tunnel syndrome can occur because exposure to HAV decreases blood flow.
Are there any solutions to make this job easier on the hands?

## Slide 53: Risk Factors
Usually occur in combinations
  Repetitive, forceful hand exertion
  Awkward back posture and heavy lifting
Notes: Risk factors usually occur in combination.
Examples: awkward back postures and lifting, or repetitive and forceful gripping.

## Slide 54: Personal Risk Factors
Age
Gender
Obesity
Health status
Hobbies & recreation
Stress
Which risk factors could be modified?
Notes: Personal factors may also increase the risk of developing various MSDs
  Age: as we get older the chances of developing a MSD becomes greater
  Gender – there are certain types of bone, joint or muscle problems that happen more to males than females or vice versa.
    What MSDs do you think males have more than females?
      Back for males
      Wrist problems and carpal tunnel for females
  Obesity
    A higher body weight means the joints are more stressed making an obese person more susceptible to musculoskeletal injury.
    As another example, relate obesity to marbled steak. Marbled steak tastes good because there is fat embedded in the muscle. Similarly, our muscles can become marbled, which makes the muscle weaker and possibly more susceptible to musculoskeletal injury.
    Obesity is also hard on our heart muscle, which can make physical activity more difficult.
  Health status – certain illnesses, such as diabetes, make a person more susceptible to musculoskeletal injury.
  Hobbies and Recreation – certain recreational activities may increase susceptibility to musculoskeletal injury.
    For example, a person who uses a floor scrubber during the week and rides a dirt bike during the weekend may not be giving their hands a break.
  Stress is also a risk factor that can make muscles work harder than they need to.
Some of these personal risk factors can not be modified, such as age and gender. Others, such as obesity and stress, are modifiable.

## Slide 55
Ergonomics
Job
Requirements
Worker
Capabilities
Notes: Ergonomics is a a constant balancing act between worker capabilities and job requirements with their inherent risk factors
  All jobs have varying degrees of risk factors.
  The goal of ergonomics is to reduce these risk factors as much as possible.

## Slide 56: Direct and Indirect Costs of Risk Factors

## Slide 57: Direct and Indirect Costs of Risk Factors
Injuries
Health care costs
Workers’ compensation
Notes: There are two kinds of costs related to poor design.
  Direct costs
  Indirect costs
“Direct costs” are those that are easiest to estimate.
  Injuries
  Health care costs such as physician visits, X-rays, physical therapy, chiropractic care.
  Worker’s compensation costs, i.e., time-loss compensation (about 60-75% of the worker’s wage).

## Slide 58: Direct and Indirect Costs of Risk Factors
Injuries
Health care costs
Workers’ compensation
$15 to $20 Billion per year
Notes: Direct costs are estimated to be 15 to 20 billion dollars per year industry wide.

## Slide 59: Direct and Indirect Costs of Risk Factors
Turnover
Re-Training
Lost Productivity
Poor Service
Poor Quality
Investigation Costs
Injuries
Health care costs
Workers’ compensation
Notes: Just like an iceberg, the majority of costs are hidden. These are “indirect” costs.
  Re-Training – when a worker is on time-loss, someone has to be trained to do this person’s job.
  Lost Productivity – a newer workers will not be as productive as an experienced worker.
  Poor Quality – likewise, quality may suffer if a replacement worker is not as experienced.
  Poor Service – again, service may ultimately suffer.
  Turnover – high turnover in a certain department may indicate that the task is too difficult for most people.
  Investigation Cost – if a worker is on time loss for longer than a month, there is a good chance an investigator will be watching the worker at home to see if they are actually injured.

## Slide 60: Direct and Indirect Costs of Risk Factors
Turnover
Absenteeism
Re-training
Lost Productivity
Poor Service
Poor Quality
Investigation Costs
$60 - $100 Billion
Injuries
Health care costs
Workers’ compensation
Notes: Indirect costs are estimated to be 4 to 5 times more than direct costs.

## Slide 61: Work-Related Musculoskeletal Disorders (MSDs)
Notes: Workers injured due to risk factors typically have what is called a “musculoskeletal disorder” (MSD).
The injury is to the musculoskeletal system and could include muscles, bones, joints, ligaments and/or nerves.

## Slide 62: Work-Related MSDs: Also Known As…
Occupational MSDs
Repetitive Strain Injuries
Repetitive Motion Disorders
Cumulative Trauma Disorders
Overuse Syndromes
Notes: MSDs are also known as:
  Occupational MSDs – because they occur at work and are due to work-related risk factors.
  Repetitive strain injuries – this is an older, but still used, term. Not all MSDs are due to the risk factor ‘repetition’ and not all MSDs injury a muscle (strain).
  Repetitive motion disorder – another older, but still used term, with the same issues as above.
  Cumulative trauma disorders (CTDs) – still another older term suggesting that MSDs are usually cumulative injuries rather than occurring from a single event. Many MSDs are the result of cumulative work-related stress. A worker could be stressing part of the musculoskeletal system for months or years, but not feel pain. Then, a single event might be the “straw that breaks the camel’s back,” and the worker notices the pain.
  Overuse syndrome – similar to CTDs, this suggests overuse rather than a single event that causes injury.
Today, ‘musculoskeletal disorders’ is the most commonly used term to describe these injuries.

## Slide 63: Work-Related MSDs: Just the Facts
33% of all workplace injuries and illnesses are MSDs
$1 out of every $3 spent on workers compensation is for MSDs
Often underreported
  “Just part of the job”
  Fear of repercussions
Most MSDs heal quickly
Notes: Here are some basic facts about MSDs.
  They account for the highest percentage of all workplace injuries and illnesses (33%).
  Likewise, the largest percentage of workers compensation dollars are spent on MSDs.
  Some believe that MSDs are over reported. However, research studies have suggested the opposite: MSDs are often underreported.
    Workers assume that work is supposed to cause pain and they put up with it.
    Workers may underreport because they fear repercussion such as losing their job.
  Although there are bad things about MSDs, the wide majority of them are minor sprains or strains that heal quickly, often without treatment.
ACTIVITY: Draw an outline of a body or a stick figure on a flip chart. Give participants stickers or a marker to indicate where they have had a work-;related MSD sometime during their work life. The majority of stickers will likely be on the low back, neck, shoulders, and wrists.

## Slide 64: Common Work-Related MSDs
Low back disorders
Carpal tunnel syndrome
Rotator cuff injury
Notes: There are many work-related MSDs but we will only talk about three common types:
  Low back disorders - includes back muscle strains, back joint sprains, and disc problems.
  Carpal tunnel syndrome (CTS) - although CTS is usually associated with office worker, grocery workers can also get it.
  Rotator cuff injuries - this injury involves the muscles and tendons in our shoulder that raise and rotate our upper arm in the shoulder socket.

## Slide 65: Common Work-Related Musculoskeletal Disorders
Notes: The next section of slides describe low back disorders, carpal tunnel syndrome, and rotator cuff injury in more detail.
Depending on the audience and comfort level of the presenter, these slides could be omitted.

## Slide 66: Low Back Disorders
Most common MSD
About 1/3 of all worker’s comp cases
33% more expensive than other time-loss claims
Worse between ages 35- 55 years old
Leading cause of disability in persons under 45
Back injuries commonly reoccur
Notes: Low back disorders:
  Are the most common MSD.
    Over 90% of people will experience low back pain some point in their life. However, having back pain does not mean that there is a MSD.
  Account for about 1/3 of all workers’ compensation cases.
  Are 33% more expensive than other time-loss claims.
  Generally become worse as we get older and are more common between 35-55 years old.
  Are the leading cause of occupationally-related disability in persons under 45 years old.
  Commonly reoccur. Once someone has a back injury, it can come back easier.

## Slide 67: The Low Back
Notes: A little anatomy lesson on the spine.
  The left picture shows a side view of the low back. Have participants reach their hand behind their low back to feel how it curves in (usually).
  The right picture shows a view of the spine from the back. Bones called ‘vertebrae’ stack on top of each other to make up the spine.

## Slide 68: The Low Back
Notes: Taking a closer look at the right side of two vertebrae, in the left picture you can see the discs between two vertebrae.
In the right picture, a view from the side and back, you can see the joints of the spine, called a ‘facet joint.’
  A ‘back sprain’ is when the ligament that holds the facet joints together is stretched.
In both pictures, you can see the ‘nerve root.’ The nerve roots turn into nerves that go down the legs. So, certain injuries to the low back can cause leg pain (similarly, certain neck injuries can cause arm pain).

## Slide 69: The Low Back
Notes: If we cut the previous picture in half, we can see that the disc is made up of two parts.
  The outside of the disc (‘annulus’) is made of rings of fiber, much like a radial tire.
    It’s job is to hold the inside ‘nucleus pulposus’ in place.
  The inside of the disc (‘nucleus pulposus’) is similar to the jelly in a doughnut.
    It acts as a shock absorber when we walk, bend, jump, etc.
    It tends to dry out as we get older which means our spine can’t absorb shock as well.
  Injuries to the disc are called ‘lumbar disc syndrome’ or ‘herniated disc.’
    Disc injuries usually involve the nucleus breaking through the annulus towards the back of the spine (to the left in the picture).
    People with disc injuries commonly complain of back and leg pain.

## Slide 70: The Low Back
Notes: This is a top view of a vertebrae and disk.
  The top of the picture is the back part of the spine.
  Have participants feel the back of their neck or the spine in the low back. They are feeling the pointy bone at the top of the picture (spinous process).
Note that the spinal cord is right behind the disc.
If the nucleus breaks through the annulus in a backward direction, the person may end up with pressure on the spinal cord, or severe back and/or leg pain from pressure on the nerve root.

## Slide 71: Low Back Disorders What are the Causes?
Notes: There are occupational and non-occupational causes of low back disorders.
Work-related risk factors associated with low back disorders include:
  Heavy lifting – lifting causes disc compression (squishes the jelly donut) and shearing (sliding forward) of one vertebrae on the other
  Awkward or stooped back postures cause both compression and shearing.

## Slide 72: Back Posture and Disc Pressure
Nachemson, 1981; Wilke et al., 1999
Notes: Studies done in 1981 by Dr. Alf Nachemson, and 1999 by Wilke and colleagues found how disc pressure is affected by different postures.
In the graph you can see that standing causes about 100 units of pressure.
  To the left, you can see that disc pressure decreases when someone lays down
  To the right, you can see that disc pressure increases with standing in a bent forward position and/or holding weight.
In general, bending forward and/or lifting increases pressure on the disc.
  Our spine is designed to handle these forces intermittently but not repeatedly.

## Slide 73: Low Back Disorders What are the Causes?
Non-occupational
  Age
  Body mass index
  General health status
  Smoking
Notes: There are also causes of low back disorders that are not related to work.
Non-occupational factors associated with low back disorders include:
  Age – as we get older, back injuries can occur more frequently and be more disabling.
  Body mass index – BMI is the ratio between body weight and height2. The higher the BMI, the more likely someone will have low back pain.
  General health status – certain diseases make people more susceptible to back pain, for example, osteoarthritis in older workers.
  Smoking – several studies have shown that smokers have more low back disorders and take longer to heal after injury.

## Slide 74: Carpal Tunnel Syndrome
“Pinched nerve” of the wrist causing hand numbness and weakness
Causes more days away from work than any other workplace injury
  Fractures ~ 17 days
  Amputations ~ 20 days
  Carpal tunnel syndrome ~ 30 days away
Notes: Carpal tunnel syndrome (CTS) is the next MSDs to discuss.
It can be considered a “pinched nerve” in the wrist.
  The nerve that is pinched controls strength and sensation in the thumb and first three fingers.
Somewhat surprisingly, CTS causes more days away from work than any other work place injury.
  Compare this to other conditions:
    Fractures – people who fracture a bone typically return to work after 17 days.
    Amputations – those who have lost a finger, or part or all of a limb are returning after 20 days.
    CTS – takes about 30 days before return to work.
Although CTS causes more time away from work, it is not as common as people think.

## Slide 75: Carpal Tunnel Syndrome
Notes: CTS involves the median nerve, which comes out of the neck and travels down the arm to the wrist.

## Slide 76
Notes: The ‘carpal tunnel’ is the space created by the wrist bones (floor of the tunnel) and the transverse carpal ligament (roof of the the tunnel).
The median nerve and flexor tendons (tendons that bend the fingers) go through the tunnel.
The median nerve can become compressed by anything that causes the tunnel to become narrower.

## Slide 77: Carpal Tunnel Syndrome What are the Causes?
Notes: There are occupational and non-occupational causes of CTS:
Potential occupational causes include:
  Forceful hand exertions, such as gripping while meat cutting. This can cause wrist tendons to expand, which can narrow the tunnel.
  Repetitive hand movements, such as at the checkout. Repetition can cause decreased blood flow around the median nerve, which can cause the nerve to not work as well.
  Hand-arm vibration, such as using a floor buffer. Vibration also reduces blood flow in the carpal tunnel. Custodians are the main grocery workers exposed to this.

## Slide 78: Carpal Tunnel Syndrome What are the Causes?
Non-occupational
  Age
  Body mass index
  General health status
Notes: There are occupational and non-occupational causes of CTS:
  Non-occupational:
    In general, older workers are more susceptible to CTS, probably again due to decreased blood flow.
    People with a higher body mass index (i.e., more obese) may have extra fluid around the wrist, which can narrow the carpal tunnel.
    Certain health conditions can contribute to CTS such as diabetes or pregnancy.

## Slide 79: Rotator Cuff Injury
Inflammation of shoulder tendons
AKA
  Impingement syndrome
  Swimmer’s shoulder
Notes: The rotator cuff is a group of four muscles that help to stabilize our shoulder.
Injuries to the rotator cuff can range from tendonitis (inflammation of the tendons) to tear of the tendons.
  The circle in the picture is showing a torn rotator cuff tendon.
Rotator cuff injuries are common in baseball pitchers and football quarterbacks.

## Slide 80: Rotator Cuff Injury What are the Causes?
Pinch zone
Notes: In grocery workers, the rotator cuff tendons usually become injured from repetitive pinching of the tendons between a shoulder bone (acromion) and the upper arm (humerus).
  This pinching occurs when people put their arm in the chicken wing position.
Repetitive pinching causes the decreased blood flow/nutrition in the tendon or ‘ischemia.’
If blood flow decreases enough, the tendon becomes weak and can tear.

## Slide 81: Rotator Cuff Injury What are the Causes?
Notes: Awkward posture of the shoulder
    Overhead work
    Chicken wing posture
What could be done to improve these postures?

## Slide 82: Indirect Costs of Work-Related Musculoskeletal Disorders
Quality of Personal Life
Notes: Work-related MSDs also affect home life.
For example, a worker who hurts his hand at work may not be able to do hobbies at home such as woodworking.

## Slide 83: Cost of Poor Design
Worker’s quality of life is reduced
Employer loses to competitors
Society pays the cost
Notes: In summary, poor workplace design affects worker’s overall quality of life, which indirectly makes the workplace less productive, and affects society as a whole.
The cost of poor design is really much bigger than you might think.

## Slide 84
Notes: Next we will talk about how to implement ergonomic programs and ergonomic solutions.
This is a good time for a break.
  Encourage participants to stand up and walk around during break.

## Slide 85: Outline
Introduction to Ergonomics
Hazards of Ignoring Ergonomics
Implementing Ergonomics and Solutions
The Ergonomics Process
Ergonomic Problem Solving

## Slide 86: Implementing Ergonomics

## Slide 87: Implementing Ergonomics
Systematic approach for improving the grocery workplace
Expert approach
Participatory approach
Notes: Ergonomics should be implemented using a systematic approach for improving the grocery workplace.
There are two basic approaches to implementing ergonomics:
  Expert approach
  Participatory approach

## Slide 88: Expert Approach
Ergonomist hired by company
Specific costs budgeted for project
Specific ergonomic solution
The problem:
  Someone else is telling you how to do your work!
Notes: The expert approach should primarily be used if…
  The grocery store has a specific solution in mind.
  An ergonomist is hired to help develop and implement the solution.
  The costs of the solution are pre-determined.
The expert approach is effective in these scenarios.
The problem with the expert approach is that someone else is telling you how to do your work.

## Slide 89: Participatory Ergonomics Approach
All employees are involved in…
  Identifying and analyzing risk factors
  Developing and implementing solutions
Leads to…
  Greater acceptance of change
  Promotion of personal responsibility for health
Ergonomic training is the first step
Notes: Participatory ergonomics is the term used when all employees (management and workers) in a company are involved in the ergonomics process.
The process involves:
  Identification and analysis of risk factors for MSDs.
  Development and implementation of ergonomic solutions.
Involvement of all employees helps to promote:
  Acceptance of changes in the work environment.
  All employees to have personal responsibility for their workplace health.
All employees must receive some training in ergonomic principles for participatory ergonomic programs to be successful.

## Slide 90
Notes: Regardless of whether an expert or participatory ergonomics approach is used, a cyclical, continuous improvement process is recommended for ergonomic improvements.
  1. Risk factors are identified.
  2. The impact of these risk factors is analyzed using ergonomic exposure assessment methods.
  3. Solutions are developed that match the risk factor.
  4. Solutions are then implemented.
  5. After a certain period of time (weeks or months), the solution is evaluated to see if the risk factor has been minimized.
    If so, the process stops for this risk factor.
    If not, the process continues with re-identification of the problem.

## Slide 91: Who is Responsible for Ergonomics?
All employees!
Ergonomic team
Safety committee
Notes: In larger grocery chains, an ergonomic team may be responsible for implementing the ergonomics process.
In smaller grocery chains, participatory ergonomics becomes part of the safety committee’s responsibility.

## Slide 92
ERGONOMICS
TEAM
WORKERS
Managers
Safety Manager
Purchasing
Human Resources
Medical Practitioners
Ergonomist
Custodians
Maintenance
Notes: Ergonomic teams should have ‘front-line’ workers and management involved.
Other key members include the safety manager, someone from purchasing and human resources, custodians, and maintenance.
Less frequently, medical practitioners such as an occupational medicine physician, physical therapist, occupational therapist, or ergonomist might be involved.

## Slide 93: Ergonomics Solutions
Notes: Next we will talk about what you implement.

## Slide 94: What is Implemented?
Ergonomic solutions
Hierarchy of solutions
Notes: Ergonomic solutions are also called ‘fixes’ or ‘controls’.
Some solutions are usually more effective than others so there is a ‘hierarchy of solutions.’

## Slide 95: Hierarchy of Solutions
Engineering solutions
Administrative solutions
Personal solutions
Most Effective
Least Effective
Notes: Engineering solutions are those that ‘engineer-out’ the risk factor. These solutions are usually the most effective in minimizing the impact of the risk factor.
Administrative solutions are those that require management to coordinate.
Personal solutions are those that require the employee to implement and are considered the least effective type of solution.

## Slide 96: Personal Solutions
Personal protective equipment
Exercise programs
Good nutrition
Proper lifting
Notes: Personal solutions are the least effective ergonomic interventions because the worker has to remember to use them.
Examples of personal solutions include personal protective equipment, exercise, good nutrition, and proper lifting.

## Slide 97: Personal Solutions: Personal Protective Equipment
Examples of PPE
  Gloves
  Goggles
  Ear plugs
  Knee pads
  Back belts
So what’s the problem?
Notes: Personal protective equipment (PPE) are personal solutions that are designed to protect a worker from hazards.
  For example, goggles may be worn while cleaning to protect the eyes from chemical splashes
Although PPE is important for reducing exposure to hazards, the worker has to remember to use the PPE.
  In other words, the hazard remains.

## Slide 98: Personal Solutions: Are Back Belts a Good Idea?
Must be used properly
  Tighten when lifting
  Loosen when not
May give false sense of security
Notes: Back belts are a type of PPE to potentially protect against back injury while lifting. They have been used for years by weightlifters.
To work properly, they must be tightened before lifting and then loosened after.
One problem with back belts is that a worker may lift greater weights with the belt than without, giving a false sense of security.
The National Institute for Occupational Safety and Health (NIOSH) stated, “Although back belts are being bought and sold under the premise that they reduce the risk of back injury, there is insufficient scientific evidence that they actually deliver what is promised.”
  This does not mean that they are NOT effective. It just means that the research community really doesn’t know.

## Slide 99: Personal Solutions: Exercise Programs
Stay fit
  Stretching
  Strengthening
  Endurance
Pre-shift stretching
Notes: Staying fit is another type of personal solution.
Three basic types of exercise exist:
  Stretching exercises.
  Strengthening exercises such as lifting a dumbbell.
  Endurance or cardiovascular exercises such as walking, bicycling, running, or swimming.
Some companies have implemented a brief pre-shift stretching program. Although there is a physiological benefit of stretching, it is uncertain if these programs help to prevent MSDs.
The problem with exercise programs is that the worker, once again, makes the change while the workplace stays the same.

## Slide 100: Personal Solutions: Good Nutrition
Eat right
Notes: Another type of personal solution is paying attention to what you eat. Since there is an established relationship between obesity and increased risk of MSDs, proper nutrition may be effective in reducing risk.
  Which might be the healthier choice?
However, like all personal solutions, the workplace hazard still remains.

## Slide 101: Administrative Solutions
Screening workers
Training workers
Job rotation
Notes: Administrative solutions are usually considered better than personal solutions.
Administrative solutions are work rules or processes that management implements.
Examples include:
  Screening workers.
  Training workers.
  Job rotation.

## Slide 102: Administrative Solutions: Screen Workers
Notes: One type of administrative solution is to screen workers.
  For example, only the strongest employees lift anything heavy (taking out garbage, produce).
However, what happens if that worker is out sick or on vacation; who does the lifting then?
Similar to personal solutions, the hazard is still present.

## Slide 103: Administrative Solutions: Train Workers about Ergonomics
Notes: Another administrative solution is training workers about workplace risk factors and how ergonomics can help.
Training has been shown to be effective in improving worker awareness and responsibility.
However, training must be repeated to be effective and, like personal solutions, the hazard remains.

## Slide 104: Administrative Solutions: Train Workers about Proper Lifting
Notes: Workers could also be trained on how to lift properly, which is both a personal solution and administrative solution.
Training workers how to lift properly is one of the most common administrative solutions used in grocery stores and is part of most any ergonomic training program.
The common phrase is, “lift with your knees, not with your back.”

## Slide 105: Administrative Solutions: Proper Lifting – Squat Lift
Notes: The left picture shows a stoop lift and the right shows a squat lift.
For heavier objects, the squat lift is recommended.
  Whatever you are lifting, keep it as close to you as possible during the lift.
ACTIVITY: Have participants practice this lift with a box weighing about 15 lbs.

## Slide 106: Administrative Solutions: Problems with the Squat Lift
“Squares the back but spoils the knees”
Physiologically more difficult than stoop lift
Squat lift not best for all lifting conditions
Notes: Although the squat lift may be effective for single lifts, it is hard on the knees and may be impossible for a worker without excellent leg strength and flexibility.
The squat lift may not be the best lifting method for larger boxes.

## Slide 107: Administrative Solutions: Proper Lifting – Golfer’s Lift
Notes: For lighter objects, you can use a “golfer’s lift” where one leg is lifted up slightly to counteract bending forward.
ACTIVITY: Have participants practice this lift by lifting a can off of the floor

## Slide 108: Administrative Solutions: Rotate Jobs & Workers
Alternate heavy and light jobs
Notes: Another administrative solution is to rotate jobs and/or workers.
These pictures show a meat cutter using forceful exertions of the hand and then rotating to a job that’s easier on the hands.
If job rotation is used, it is important that the worker is not exposed to the same risk factor.

## Slide 109: Engineering Solutions
Workspace
Posture
Manual materials handling
Seating
Notes: Engineering solutions are the best way to reduce exposure to risk factors in the grocery store.
Why? (the hazard is ‘engineered’ out, worker does not need to remember to do something to lower the risk).
Engineering solutions include changes to any of the modifiable workplace factors that were first covered in this training.

## Slide 110: Engineering Solutions: Get Product Off the Floor
Stack of pallets
Scissors lift pallet jacks
Notes: Instead of having workers repetitively “lift properly,” get product off of the floor by using an engineering solution such as:
  A stack of pallets if a forklift is available.
  Scissors lift pallet jacks
The worker can then keep heavy lifting between knee and chest height, which is the safest region for lifting.

## Slide 111
Notes: To help the participants practice developing solutions, use a a video clip on YouTube of woman falling through trap door. Use search words “funny fall” (although the situation is serious and not very funny) or link to: http://www.youtube.com/watch?v=w5jsV_YENPk
In groups of 2 – 4, have participants take about 10 minutes to come up with a list of several personal, administrative, and engineering solutions.
  List the benefits and the problems of each solution.
Possible solutions:
  Personal solutions: all employees wear protective padding so they aren’t hurt when they fall, teach employees to fall properly.
  Administrative solutions: train all employees to look behind them before moving, rotate workers to “balance out the risk” (everyone has a chance to fall!).
  Engineering solutions: siren sounds and light flashes when door is open, railing around door, spring-loaded door close, or move the door (best).
Discuss pros and cons of all solutions (practicality, ease of implementation, cost)

## Slide 112
Notes: What is the risk factor(s)? (awkward postures of the back and possible heavy lifting)
What part of the body could be injured? (low back, shoulders)
What are possible personal, administrative, and engineering solutions for this grocery worker?
  Personal solutions: back strengthening program, back belt.
  Administrative solutions: instruction in proper lifting, job rotation.
  Engineering solutions: box with fold down sides, smaller produce boxes, put box on higher pallet

## Slide 113
Notes: A possible personal solution for lifting lighter weights is the “golfer’s lift.”
One leg is lifted slightly to counteract the forward bending of the back.

## Slide 114
Notes: Next we will go through the Ergonomics Process step by step.
This is a good time for a break.
  Encourage participants to stand up and walk around during break.

## Slide 115: Outline
Introduction to Ergonomics
Hazards of Ignoring Ergonomics
Implementing Ergonomics and Solutions
The Ergonomics Process
Ergonomic Problem Solving

## Slide 116
Notes: As previously mentioned, the Ergonomics Process is a cyclic, continuous improvement, process.

## Slide 117
Notes: The first step of the process is to identify that there are ergonomic issues in the store.

## Slide 118: How to Identify Problems
Worker complaints
Known risk factors
Injury reports
Medical & insurance costs
Work absence
Customer complaints about product or damaged product
Notes: There are several ways managers or the safety committee might identify problems:
  If workers continually complain of pain or difficulty while performing a certain task, the work may be problematic.
  There may be risk factors that everyone knows exist. As an example, where are the heaviest products typically shelved? (return to dog food example).
  Review injury reports to see if several injuries are occurring in a specific department or task.
  Review workers’ compensation claims.
  If workers are frequently absent in a certain department, it could be that the work is too difficult.
  If customers are complaining that, say, the watermelons don’t last long enough, it could be that the produce workers are dropping them because they are lifting too much.

## Slide 119
Notes: The second step is to analyze the task.

## Slide 120: Analysis
Discussions with workers
“If you could change one thing about your job what would it be?”
Notes: Analysis starts by asking workers about the stresses associated with the tasks they do.
  A good way to gain this information is to ask, “If you could change one thing about your job, what would it be?”
Successful participatory ergonomics programs encourage worker involvement so discussions with workers is an important step.

## Slide 121: Analysis
Observation
Ergonomic job analysis
Notes: It is also important to observe, possibly with a video camera, potentially hazardous tasks.
  A safety committee could have an ‘ergonomic walk-around’ during a meeting time.
A more formal ergonomic job analysis can also be done, such as using a checklist.

## Slide 122: Ergonomic Job Analysis Step 1
Prioritize jobs for change
Notes: The first step of ergonomic job analysis is to prioritize jobs for change.
Since there is not unlimited time or resources, and changing all jobs would be cost prohibitive, prioritization helps to make the Ergonomics Process more realistic.
You can use an ergonomic job analysis method to prioritize jobs. We will show you how to use the Rodgers Muscle Fatigue Analysis for prioritization.

## Slide 123: Ergonomic Job Analysis Step 2
Identify risk factor(s) in the job
Notes: The second step of ergonomic job analysis is to accurately identify which risk factors are present.
This step is important because ergonomic solutions must reduce exposure to risk factors in order to be effective.

## Slide 124: Ergonomic Job Analysis Step 3
Quantify the risk factor(s)
  Effort level – How hard is the task?
  Effort duration – How long does the task take?
  Effort frequency – How often is the task done?
Notes: The third step of ergonomic job analysis is to quantify the risk factor.
There are three parameters of any risk factor:
  Level
  Duration
  Frequency
Here is an example of these parameters while stocking dog food:
  Level: heaviest bag is 35 lbs.
  Duration: restocking the shelves may take 10 minutes.
  Frequency: during the 10 minutes, 50 bags are stocked giving a frequency of 5 lifts per minute.
Often, one of the parameters is the greatest hazard.
  For example, lifting a 150 lb weight (level) one time (frequency) may be more hazardous than lifting 10 lbs. 15 times.

## Slide 125: Ergonomic Job Analysis Tools to Quantify the Risk Factor(s)
Different tools depending on the risk factor
Dr. Thomas Bernard’s website of ergonomic analysis methods
All risk factors
  Rodgers Muscle Fatigue Analysis
http://personal.health.usf.edu/tbernard/ergotools/index.html
Notes: There are many methods to perform an ergonomic job analysis.
  Each method assesses certain risk factors so it is important to match the method with the risk factor.
Dr. Thomas Bernard, a professor at the University of South Florida, maintains an excellent website of ergonomic analysis tools. The link is at the bottom of the slide or you can search for, “Thomas Bernard Ergonomics.”
A method that can be used to assess many risk factors is called the Rodgers Muscle Fatigue Analysis (RMFA).
A method that can be used to assess if a weight is too much to lift is called the WISHA Lifting Analysis.
Ergonomics Process Training could include either or both of these analysis methods.

## Slide 126: Rodgers Muscle Fatigue Analysis
Notes: If teaching this method, make copies for all participants. You can download copies by going to Dr. Thomas Bernard’s link

## Slide 127: Rodgers Muscle Fatigue Analysis
Analyzes all body regions
Analyzes most risk factors
Theory: rapidly fatiguing muscle → injury
Outcome: “priority for change”
-Rodgers, 1988
Notes: RMFA assesses all body regions affected by musculoskeletal disorders.
RMFA indirectly assesses the following risk factors, depending on the body region:
  Heavy lifting
  Awkward postures
  Static postures
  High repetition
  Forceful hand exertions
RMFA does not assess:
  Hand-arm vibration
  Personal factors
The theory of RMFA is that a rapidly fatiguing muscle can lead to musculoskeletal injury.
The result of doing a RMFA is called a “priority for change.”
  Basically, this method can help the analyst look at several tasks in the grocery store and then decide which tasks should be modified.

## Slide 128
-Rodgers, 1988
Notes: Here is an example of the RMFA.
The RMFA seems complicated but is quite easy to use.
Participants should be given copies of this method for practice.

## Slide 129: How to Use the Rodgers Muscle Fatigue Analysis
Observe a task that lasts longer than 10% of the shift
Determine which regions of the body are most stressed
Rate effort, duration, and frequency for those regions to make a three-digit index.
Compare results to a table
Score as low, moderate, high, very high priority
Notes: 1. Only look at tasks that last at least 10% of the shift.
  For example, dumping garbage only takes a few minutes so a different analysis method would be used to assess this task, such as the Utah Back Compressive Force.
2. The observer watches the task and then estimates which part(s) of the body would be most stressed while performing the task.
  For example, cashiering probably stresses the wrist, hands, and fingers most and then the arms and elbows.
    So, the RMFA could only be done for these two regions.
3. For each body region, the three parameters of a risk factor (effort level, duration, and frequency) are rated. You will get three numbers, or an ‘index,’ from this step.
4. You use a table to evaluate the index.
5. Based on the table, the task can be rated as low, moderate, high, very high priority.
  It is important to develop solutions for high and very high priority tasks.

## Slide 130: Rodgers Muscle Fatigue Analysis
Notes: This is the top half of the RMFA.
Write in the job and task.
  ‘Job’ might correspond to ‘dairy department’ and ‘task’ might be ‘stocking milk.’
Analyst is the person performing the analysis.
% of shift time is an estimate of the daily duration performing the task.

## Slide 131: Rodgers Muscle Fatigue Analysis
Notes: As an example of how to do a RMFA, rate the right shoulder (red arrow) of someone stocking milk.
  For shoulders, the risk factors that are analyzed include awkward postures, forceful exertions/heavy lifting, static postures, and repetition.
Note that for each body region, you will enter 3 scores in the ‘Scores’ columns. These 3 scores make the index which is compared to a table.
Note that you rate the right and left sides separately for some body regions, like the shoulders. Pick the side that seems to be working the hardest.

## Slide 132: Rodgers Muscle Fatigue Analysis 1. Rate Effort Level
Notes: 1st rate the effort level (yellow highlighting).
  Effort level is rated a 1 if light, 2 if moderate, 3 if high, and 4 if very high. Note that a VH (very high) rating is effort that can’t be exerted by most people.
In our example, stocking milk definitely requires holding a weight (milk jug) with the arms away from the body, so this is considered a ‘heavy’ effort level or 3.
  Most people could probably stock milk, at least for a short period of time, so you would not rate this task as ‘very high’ or 4.

## Slide 133: Rodgers Muscle Fatigue Analysis 1. Rate Effort Level
3
Notes: Put the number corresponding with the effort level in the first score box under ‘right’ since that is the side you are rating.

## Slide 134: Rodgers Muscle Fatigue Analysis 2. Rate Duration
Notes: 2nd rate the duration of a continuous effort (Dur) for the right shoulder.
  Duration means how long a continuous exertion, such as lifting one milk jug, lasts without rest.
  Use the second to last row at the bottom of the RMFA (yellow highlighting) to rate this part of the index.
  Continuous effort duration is rated a 1 if the exertion is held for less than 6 seconds, 2 if 6-20 seconds, 3 if 20-30 seconds, or 4 for > 30 seconds.
In our example, a milk jug is probably held for less than 6 seconds, so this is scored a 1.

## Slide 135: Rodgers Muscle Fatigue Analysis 2. Rate Duration
3
1
Notes: Put the number corresponding with the continuous effort duration in the second score box under ‘right’ since that is the side you are rating.

## Slide 136: Rodgers Muscle Fatigue Analysis 3. Rate Frequency
Notes: 3rd rate the effort frequency (Freq) for the right shoulder.
  Effort frequency means how many exertions are made in one minute.
  Use the last row at the bottom of the RMFA (yellow highlighting) to rate this part of the index.
  Effort frequency is rated a 1 if there is less than 1 effort in one minute, 2 if 1-5 efforts per minute, 3 if 5-15 efforts per minute (one effort every 12 seconds to one effort every 4 seconds), or 4 if more than 15 efforts per minute.
In our example, between 5 and 15 milk jugs are stocked in 1 minute, so this is scored a 3.
NOTE: if effort frequency increases, effort duration decreases and vice versa.

## Slide 137: Rodgers Muscle Fatigue Analysis 3. Rate Frequency
3
1
3
Notes: Put the number corresponding with the effort frequency in the third score box under ‘right’ since that is the side you are rating.
You now have the RMFA index and need to compare this to a table.

## Slide 138: Rodgers Muscle Fatigue Analysis “Priority for Change” Tables
Notes: 313 is in the ‘high’ priority for change column.
So, at least for the right shoulder, the ergonomics committee along with workers in the dairy department might develop solutions to reduce this index.

## Slide 139: Rodgers Muscle Fatigue Analysis: So What Do You Change?
Look at the tasks that are high or very high priority for change
Look at the highest number(s) of the index and modify that parameter
  Effort level
  Effort duration
  Effort frequency
Notes: The highest numbers of the index provide a clue as to what parameter could contribute most to injury.
In our example, both effort level and frequency were 3s.
  Example of solutions to impact effort level:
    Lower milk racks or have employee stand on a platform so the arms are not away from the sides as much.
    Rollers on milk racks so milk jugs do not need to be held longer than needed.
      What kind of solutions are these? (engineering)
  Example of solutions to impact effort frequency:
    Rotate workers through this task.
      What kind of solution is this? (administrative)

## Slide 140: WISHA Lifting Analysis
Notes: If teaching this method, make copies for all participants. You can download copies by going to Dr. Thomas Bernard’s link
The WISHA Lifting Analysis is only used to assess lifting

## Slide 141: WISHA Lifting Analysis
Notes: Here is an example of the WISHA Lifting Analysis.
This method seems complicated but is quite easy to use.

## Slide 142: WISHA Lifting Analysis
Developed by Washington L&I
Is the weight lifted hazardous?
Notes: This method was adapted from the NIOSH Lifting Equation (available http://www.cdc.gov/niosh/docs/94-110/).
The method is used to answer the question, “Is the weight lifted hazardous?”

## Slide 143: How to Use the WISHA Lifting Analysis
Find out the weight of what’s lifted
Determine the position of the worker’s hands at the beginning of the lift
Find out the frequency and duration of lifting
See if the worker has to twist during the lift
Determine if the lift is a hazard
Notes: 1. Find out the weight of the object.
  Only evaluate objects weighing more than 10 lbs.
2. A graph is used for this step.
3. Find out how many lifts are done per minute and how long these lifts take in a day.
4. Watch a worker perform the lift to see if they have to twist.
5. The last step determines if the lift is hazardous.
The following slides will go through each step.

## Slide 144: WISHA Lifting Analysis Step 1: Weight of Object Lifted
Notes: In this example, a worker is lifting a 40 lb. bag of dog food from the pallet and stocking it on the shelf.
  This is called the “Actual Weight.”
Write this weight on the form in Step 1.
  Actual Weight = 40.

## Slide 145: WISHA Lifting Analysis Step 2: Beginning Hand Position
Notes: In this example, the worker’s hands are about 12” away from an imaginary vertical line and the lift is starting below the knee. This gives a value of 35.
  This number is called the “Unadjusted Weight Limit.”
Write this number on the form in Step 2.
  Unadjusted Weight Limit = 35.

## Slide 146: WISHA Lifting Analysis Step 3: Frequency & Duration
Notes: In this example, the worker is performing 1 lift every minute for 1 hour or less. This gives a value of 0.95.
  This is called the “Limit Reduction Modifier.”
Write this number on the form in Step 3.
  Limit Reduction Modifier = 0.95.

## Slide 147: WISHA Lifting Analysis Step 4A: Is the Worker Twisting?
Notes: In this example, the worker appears to be twisting more than 45 degrees during the lift.
The angle is determined by seeing if the shoulders line up with the hips.
If the twist is a lot (more than 45 degrees as in the picture on the right), you will multiply the “unadjusted weight limit” by 0.85.
  This is called the “Twisting Adjustment.”
Write this number on the form in Step 4.
  Twisting Adjustment = 0.85.
If the twist is a little (less than 45 degrees), the twisting adjustment remains blank.

## Slide 148: WISHA Lifting Analysis Step 4B: Adjusted Weight Limit
More than 45°
Less than 45°
Unadjusted Weight Limit  0.85 =
Adjusted Weight Limit
Unadjusted Weight Limit =
Adjusted Weight Limit
Notes: In this example, the worker appears to be twisting more than 45 degrees during the lift.
Calculate the “Adjusted Weight Limit.”
  35 × 0.85 = 29.75
Write this number on the form in the third line of Step 4.
  Adjusted Weight Limit = 29.75.
  (if the twist was less than 45 degrees, Adjusted Weight Limit = Unadjusted Weight Limit).

## Slide 149: WISHA Lifting Analysis Step 4C: Calculate Weight Limit
Notes: Calculate the “Weight Limit” by multiplying the “adjusted weight limit” by the “limit reduction modifier.”
  29.75 × 0.95 = 28.3
Write this number on the form in the fifth line of Step 4.
  Weight Limit = 28.3.
  (if the twist was less than 45 degrees, Weight Limit = 35 × 0.95 = 33.3).

## Slide 150: WISHA Lifting Analysis Step 5: Is the Lift Hazardous?
28 lbs if twisting
33 lbs if not
vs.
40 lbs
Notes: This last step determines if the lift is potentially hazardous.
The lift is hazardous if the “Weight Limit” is less than the weight of the “Actual Lift.”
The lift is not hazardous if the “Weight Limit” is more than the weight of the “Actual Lift.”
Since the “Weight Limit” is 28 to 33 lbs., the lift is considered hazardous.

## Slide 151: WISHA Lifting Analysis So What Do You Change?
Is the weight the problem?
Is the reach distance the problem?
Is the frequency or duration the problem?
Notes: If the lift is considered hazardous, you should determine if the weight, distance, frequency, or duration are the problem.
  For example, if the Actual Weight is fine but the object is lifted 10 times per minute for 2 hours, the frequency and duration are the problem.
  In this case, one solution might be to rotate this lifting task among several workers.

## Slide 152
Notes: The next step of the Ergonomics Process is to develop solutions.

## Slide 153: Develop Solutions
Hierarchy of solutions
  Best
  Better
  Good
Notes: Remember that solutions that engineer-out the risk factor are the best, administrative solutions like job rotation are second best, and personal solutions are least effective.
Examples of possible solutions are available on a free OSHA document, “Ergonomics - Guidelines for Retail Grocery Stores.”

## Slide 154: Develop Solutions Storewide
Remind workers to “put it in neutral”
OSHA, 2004
Notes: Some solutions can be used throughout the store.
For example, the OSHA booklet suggests using neutral postures whenever possible

## Slide 155: Develop Solutions Department
Front end
  If scanning fails after two attempts, key in the code
    What kind of solution?
Deli
  Front-opening display cases
    What kind of solution?
OSHA, 2004
Notes: Other solutions are specific for certain departments.
Cashiers should be taught to key in the code if hand scanning fails after two attempts.
  This is an administrative solution since it requires training (and retraining).
The deli could have a display case that opens from the front. The deli worker could walk around to easily access product in the front.
  This is an engineering solution because the reach into the case is ‘engineered out.’

## Slide 156: Develop Solutions Department
Stocking
  Knee pads
    What kind of solution?
Produce
  Keep heavy product (watermelons, pumpkins) in original containers
    What kind of solution?
OSHA, 2004
Notes: Stockers could be provided knee pads so they can kneel instead of bending over.
  This is a personal solution (ask participants where this is on the hierarchy of solutions)
Heavy produce, such as watermelons, could be kept in the original containers and moved by pallet jack to their location on the floor.
  This is an engineering and administrative solution.

## Slide 157
Notes: The next step of the Ergonomics Process is to implement solutions.
  In this step, be sure to get “buy in” from the employees who will be most affected by the solution. It’s best to have these individuals involved in the development process.

## Slide 158: Implementing Ergonomic Solutions
Easiest?
Most serious?
Least costly?
Existing vs. new?
Notes: There are no set rules on which ergonomic solutions should be implemented first.
Use of an ergonomic analysis method such as the RMFA can help you prioritize where you should focus first.

## Slide 159: Implementing Ergonomic Solutions
Does the solution change the risk factor???
  Solutions may not completely eliminate
  Continuous improvement
Think…
  Quick fix
  Long term
Notes: It’s critical that the solution somehow reduces the risk factor.
  However, in many or most cases, the risk factor can’t be completely eliminated
  Instead, take it a step at a time and change what you can, reevaluate, and modify again
When deciding about solutions, think about if it is a quick fix or a long term solution.
  Quick fixes should be considered a temporary solution until a better one is implemented.
  Long term solutions have been tested to be sure they are effective.

## Slide 160
Notes: The final step of the Ergonomics Process is to evaluate the effectiveness of the solution.
  Ergonomic committees can use the same methods they used to analyze the risk factor such as talking to employees or using an ergonomic analysis method (RMFA or other).
  The goal is that the solution should have reduced the hazard.
    If the hazard is not reduced, go through the Ergonomic Process again.
      Remember that this is a process of continuous improvement.
    Be sure a new hazard has not been introduced.
      Example: a store purchases a scissors lift pallet jack to move freight but the wheels damage the floor. The custodian now has to work harder to clean and buff this part of the store.

## Slide 161
Notes: Next we will go through the Ergonomics Process with specific tasks in the grocery store.
This is a good time for a break.
  Encourage participants to stand up and walk around during break.

## Slide 162: Outline
Introduction to Ergonomics
Hazards of Ignoring Ergonomics
Implementing Ergonomics and Solutions
The Ergonomics Process
Ergonomic Problem Solving

## Slide 163: Ergonomic Problem Solving
Work through Ergonomics Process
Notes: The last step of Ergonomics Process Training is to work through actual examples in your grocery store/chain using the following steps:
  Use the RMFA to prioritize tasks that could be modified.
  Video record tasks that are prioritized ‘high’ and ‘very high.’ If possible, video at least 5 minutes of these tasks.
  Perform an ‘Ergonomic Job Analysis’ by following the instructions on the next slides.
(As an alternative, the Washington State WISHA Screening Tool could be used to see if there are any caution or hazards in the workplace. Video record the tasks checked as a ‘caution’ and ‘hazard.’

## Slide 164: Ergonomic Job Analysis
Identify primary task
Identify the risk factors
Identify the part(s) of the body that is stressed
Identify possible solutions
  Hierarchy of solutions
  Solution should address the risk factor(s)
Identify the benefits of the solution
Identify effect on productivity
Identify obstacles to implementation
Notes: To be effective, ergonomic job analysis should be systematic approach.
It is important to clearly identify the primary task.
Identify the risk factors. Review the 7 primary risk factors found in grocery stores and use the Rodgers Muscle Fatigue Index
Be sure to understand which part of the body could be injured by the risk factor.
Identify possible solutions.
  Try to identify engineering, administrative, and personal solutions but remember that engineering solutions are often the best to implement.
  Solutions should not be randomly tried. Instead, attempt to match the solution with the risk factor.
Identify how the solution will benefit the worker and store.
Identify how the solution might influence productivity. The solution could have a positive or negative effect.
Identify potential obstacles to implementing the solution.
  Examples: cost of solution, worker acceptance, interferes with customer service, etc.

## Slide 165
Risk factors:
Area of body:
Solutions (engineering, administrative, personal):
Benefits:
Productivity issues:
Obstacles:
Primary Task: ____________________

## Slide 166
Any Questions??

## Slide 167: This training was developed by Dan Anton, PT, PhD, ATC Eastern Washington University Department of Physical Therapy dan.anton@ewu.edu

## Slide 168: Contributors
Douglas Weeks, PhD
Daniel Hansen, DC
Brian Coleman, SPT
Steve Goldrick, DPT
Laura Hall, SPT
Sam Herman, SPT
Julianne Keenan, SPT
Samantha Modderman, DPT
Blake Novoa, DPT
Christine Olsen, DPT
Notes: These are the additional research team members who contributed to this training program.

## Slide 169: Acknowledgements
This project was funded by Washington State Department of Labor & Industries Safety and Health Investments Project
  SHIP Grant 2009XH00128
Management and employees of Yoke’s Fresh Markets, Spokane, WA
Certain slides used with permission of Dr. Thomas Cook, University of Iowa and Dr. John Rosecrance, Colorado State University