## Slide 1
LEAD, ASBESTOS, SILICA, & MOLD
REQUIREMENTS AND BEST PRACTICES FOR RESIDENTIAL CONTRACTORS IN WASHINGTON
Funding and support for this project provided by State of Washington, Department of Labor and Industries, Safety and Health Investments projects.
HEALTH HAZARDS
IN CONSTRUCTION

## Slide 2
HEALTH HAZARDS IN RENOVATIONS
Your renovation job:
  1940’s home with water damage from upstairs leak
  Wet “popcorn” ceiling
  Lead Based Paint
  Mold growing from the leak
  Need to cut concrete to replace mainline into the building
Notes: On any typical remodel job, a Contractor with Employees can be faced with hazards from the materials in the building. Let’s say a General Contractor is hired to fix a basement in a 1940’s home that has ceiling water damage from an upstairs leak. After doing a quick walk thru, the Contractor notices wet “popcorn” ceiling that needs to be removed or repaired, possible lead based paint, mold growing from the leak, and he knows he may have to cut some concrete to replace a mainline into the building.

## Slide 3
HEALTH HAZARDS IN RENOVATIONS
Safety and Health Hazards?
Agencies and Rules?
Licenses and Certifications?
Training?
Equipment?
PPE?
Notes: At first it may seem confusing and too much information, but the goal is to give contractors and workers enough information to make the decisions on what scope of work they will do and can do by law. Contractors need to know all this to do a “simple remodel”.
Unfortunately, there is no single source for all this information and most agencies do not inform Contractors of the requirements. Believe it or not, it’s the Contractor’s job to research regulations to see which one’s apply to them. This document and any training provided, will help all involved see the complexity and requirements of remodeling.

## Slide 4
HEALTH HAZARDS IN RENOVATIONS
Requirements for Asbestos are similar to Mold Best Practices
Requirements for Lead Based Paint renovations are similar to Silica exposure Best Practices
Notes: Requirements for Asbestos abatement are almost identical for Mold remediation best practices and requirements for Lead Based Paint renovations are similar for Silica exposure best practices. In most cases, the equipment a contractor invests in for one hazard can be used for the other health hazards.
If Contractors learn these fundamentals of protecting workers, they can cost effectively and safely take on a huge variety of remodel projects.

## Slide 5
CONTAINMENT
PERSONAL PROTECTIVE EQUIPMENT
LOW DUST WORK PRACTICES
DECONTAMINATION
FOUR PRINCIPALS OF PROTECTION
These four concepts will help contractors address a variety of hazards and protect themselves and workers.
Notes: Here is the good part, though there are many agencies and regulations involved, everyone’s goal is the same, protect workers from health hazards. And though the hazards of asbestos, lead, mold, and silica are regulated differently, the worker protection concepts are the same. If Contractors set up the job with proper containment, use low dust work practices, wear appropriate PPE, and decontaminate, everyone goes home safe.

## Slide 6
Discuss the hazards associated with asbestos, lead, mold and silica
List the agencies and regulations that apply to the hazards
Demonstrate how proper containment, low dust work practices, appropriate PPE, and decontamination can protect worker from all four hazards
COURSE OBJECTIVES

## Slide 7
Asbestos Awareness two hour training
Lead in Construction awareness training
COURSE OBJECTIVES

## Slide 8
PLAY HEALTH HAZARDS IN CONSTRUCTION OVERVIEW VIDEO

## Slide 9
DEFINITIONS

## Slide 10
PERMISIBLE EXPOSURE LIMIT
Permissible Exposure Limits (PEL):
  PELs are the measured amount of a substance you can be exposed to over an 8 hour time weighted average (TWA) without wearing a respirator.
  Actual exposures are measured by air monitoring and compared to the PEL to determine respiratory protection needed.
Notes: From Wikipedia: The permissible exposure limit (PEL or OSHA PEL) is a legal limit in the United States for exposure of an employee to a chemical substance or physical agent. For chemicals, the chemical regulation is usually expressed in parts per million (ppm), or sometimes in milligrams per cubic meter (mg/m3). Units of measure for physical agents such as noise are specific to the agent. Permissible exposure limits are established by the Occupational Safety and Health Administration (OSHA). Most of OSHA’s PELs were issued shortly after adoption of the Occupational Safety and Health (OSH) Act in 1970, and have not been updated since that time. Section 6(a) of the OSH Act granted the Agency the authority to adopt existing Federal standards or national consensus standards as enforceable OSHA standards. Most of the PELs contained in the Z-Tables of 29 CFR 1910.1000 were adopted from the Walsh-Healy Public Contracts Act as existing Federal standards for general industry. These in turn had been adopted from the 1968 Threshold Limit Values (TLVs®) of the American Conference of Governmental Industrial Hygienists (ACGIH®).
A PEL is usually given as a time-weighted average (TWA), although some are short-term exposure limits (STEL) or ceiling limits. A TWA is the average exposure over a specified period of time, usually a nominal eight hours. This means that, for limited periods, a worker may be exposed to concentration excursions higher than the PEL, so long as the TWA is not exceeded and any applicable excursion limit is not exceeded. An excursion limit typically means that "...worker exposure levels may exceed 3 times the PEL-TWA for no more than a total of 30 minutes during a workday, and under no circumstances should they exceed 5 times the PEL-TWA, provided that the PEL-TWA is not exceeded." [1] Excursion limits are enforced in some states (for example Oregon) and on the federal level for certain contaminants such as asbestos.
A short-term exposure limit is one that addresses the average exposure over a 15-30 minute period of maximum exposure during a single work shift. A ceiling limit is one that may not be exceeded for any period of time, and is applied to irritants and other materials that have immediate effects.

## Slide 11
PELs AND RESPIRATORS
Respirators are needed when:
  If exposure to a worker exceeds the PEL, they must wear a respirator in addition to engineering controls to be adequately protected.
  Respirators have an Assigned Protection Factor (APF):
  There is a relationship between PELs and Respirator Choice
Up to 10x the PEL | Half Face Respirator
Up to 50x the PEL | Full Face Respirator
Up to 1000x the PEL | Supplied Air Full-facepiece and designed to operate in pressure-demand or other positive-pressure mode
Each respirator needs a P100 or HEPA filter attachment to be 99.97% efficient to .3 micro to protect workers from particulate health hazards.
Notes: A half-mask respirator is good to 10x the PEL of dust, mists, gases, vapors or fumes. A full-face respirator is good to 50x the PEL and a supplied Air respirator is good to 1000x the PEL. The higher the APF, the more protection it gives the worker. We will discuss this again later in the PPE section. The idea here is to understand that there is a relationship between PELs and choice of respirator.

## Slide 12
DANGER: ASBESTOS

## Slide 13
ASBESTOS
ASBESTOS:
Naturally occurring fibrous mineral
Properties include good tensile strength, flexibility, and insulating abilities
Heat, electrical and chemical resistant
When the product is ‘friable’ or breaks up, tiny invisible asbestos fibers are released into the air
These microscopic fibers are easily breathed in
Notes: Asbestos:
Asbestos is a naturally occurring fibrous mineral in several different forms (Chrysotile “white”, Amosite “brown”, Crocidolite “blue”)
It’s properties include good tensile strength, flexibility, and insulating abilities. It is also heat, electrical and chemical resistant.
Route of Entry:
When bound within a product there is little danger, but when the product is ‘friable’ or breaks up, tiny invisible asbestos fibers are released into the air. Asbestos fibers are easily breathed in by workers while working with materials containing asbestos.
Asbestos fibers are deposited in the ending small air sacs in the lungs called the alveoli.
The body’s defense mechanisms cannot break down the fibers and scar tissue forms around the fibers.
As scar tissue builds up the lungs function less and less efficiently
The fibers may also travel to the pleura, the membrane lining the outside of the lungs, causing a similar problem.
Health Effects:
Diseases caused by Asbestos:
Asbestosis
Mesothelioma
Lung Cancer
Other cancers

## Slide 14
ASBESTOS DEFINITIONS
How Much Asbestos Matters?
Asbestos Containing Material (ACM):
    Material containing more than 1% Asbestos by weight
Presumed Asbestos Containing Material installed prior to 1981 (PACM)
    Surfacing Materials
    Thermal System Insulation
    Flooring
    The Permissible Exposure Limit (PEL) for asbestos in construction is:
    .1 fiber/cc per 8 hour TWA
    1 fiber/cc per 30 min Short Term Exposure Limit (STEL)

## Slide 15
Asbestos fibers, high magnification
Common Types of Asbestos:
Chrysotile - “White asbestos”
Amosite - “Brown asbestos”
Crocidolite - “Blue asbestos”
Less Common Types of Asbestos:
Tremolite (sometimes found in vermiculite)
Actinolite
Anthophyllite
TYPES OF ASBESTOS

## Slide 16
Pipe insulation
Surfacing insulating materials
Reinforcement of materials
Fireproofing
Acoustic and decorative plaster
Textiles
Asbestos insulated pipe
Asbestos insulated boiler
Asbestos has been used for centuries, but greatly increased during and after World War II in ship insulation and the following:
Use has greatly declined since the late 1970’s
USES OF ASBESTOS

## Slide 17
These products may be found in homes and buildings constructed before 1981.
Sheet vinyl containing asbestos
Sprayed-on fireproofing material
Vinyl asbestos flooring
ASBESTOS CONTAINING MATERIALS

## Slide 18
Vermiculite insulation in attics
VERMICULITE
Research “Libby Montana”
for more information
on asbestos
poisoning
of a whole
community.

## Slide 19
This damaged pipe insulation is a health hazard to persons working around it, handling it or removing it. Asbestos fibers are visible on the torn edges.
DAMAGED ASBESTOS PIPE INSULATION

## Slide 20
Asbestos millboard was used in the construction of walls and ceilings, especially around furnaces and wood-burning stoves, where insulation and fire protection was required. Most varieties of asbestos millboard typically contained between 80% and 85% asbestos.
ASBESTOS MILL BOARD

## Slide 21: Asbestos gaskets– may be round, flat or impregnated with waterproof sealant
Asbestos fabric in HVAC system
Damaged asbestos gasket
ASBESTOS IN GASKETS & FABRIC

## Slide 22
ASBESTOS ROOFING MATERIAL

## Slide 23
Cement-asbestos pipe, sometimes called Transite, was used underground and above ground in years past and may show up in pipe replacement jobs, building demolition jobs or excavations.
CEMENT-ASBESTOS PIPE (TRANSITE)

## Slide 24
Close-up of Tile
ASBESTOS CEILING TILE
Used until about 1980. Usually white and in 1’x1’ or 2’x4’ sizes

## Slide 25
Found in older houses – not to be confused with newer asbestos-free cement siding. There is little hazard unless disturbed. The top right hand picture shows a siding replacement job with broken green asbestos shingles which would have released dust and fibers into the air if done incorrectly.
ASBESTOS SHINGLES AND SIDING

## Slide 26
Damaged ceiling material
Uncontrolled popcorn ceiling removal job
Popcorn ceilings (also known as acoustic ceilings) were popular in many homes built from the late 1950s through the early 80s. Not all popcorn ceiling material contained asbestos, but some did. Many types were more easily dislodged than others.
ASBESTOS “POPCORN” CEILING MATERIAL

## Slide 27
See WRD 23.30 for guidance on employee exposure to joint compounds
Some joint compound contained up to 5% asbestos
Joint compound
Plaster with asbestos
JOINT COMPOUND AND PLASTER
Notes: Some joint compound contained up to 5% asbestos. Older plasters in lathe and plaster construction also sometimes contained asbestos.

## Slide 28
THE DANGERS OF ASBESTOS
ASBESTOS IS COMMONLY FOUND IN:
Pipe Insulation
Surface Insulating Materials
Reinforcement of Materials
Fireproofing
Wall Board
Acoustic ceilings (Popcorn Ceilings)
Textiles and Fabrics
Vinyl Asbestos Tile (VAT)
Soft vinyl backing
Adhesives
Gaskets
Joint compound and plaster
Roofing shingles and felt
Elevator Equipment Panels
Elevator Brake Shoes
HVAC Duct Insulation
Boiler Insulation
Breaching Insulation
Ductwork Flexible Fabric Connections

## Slide 29
THE DANGERS OF ASBESTOS
Health Effects:
Diseases caused by Asbestos:
- Asbestosis
- Mesothelioma
Lung Cancer
Other cancers
Symptoms may take 15 to 30 years or more to develop
Health effects may continue to progress even after exposure is stopped
Notes: What you need to know about asbestos:
Removal or disturbing of Surfacing Materials, Thermal System Insulation is considered very dangerous and can release large amounts of asbestos into the air.
Other products such as rolled vinyl flooring, vinyl asbestos tiles, mastics or adhesives (often black), plasters, roofing materials, and gaskets also contain asbestos. Working with these products can also cause exposure to workers.
Very small amounts of asbestos can cause chronic effects in all people that are exposed, including contractors, workers, and homeowners.
Workers can bring asbestos-contaminated dust home and poison their families.

## Slide 30
Lung cancer causes the largest number of deaths from asbestos exposure. The risk greatly increases in workers who smoke.
LUNG CANCER

## Slide 31
Esophagus
Larynx
Oral cavity
Stomach
Colon
Kidney
Evidence suggests that ingesting asbestos can also cause cancers in the:
Fibers can enter the mouth and be swallowed. Poor hygiene, leaving food/drinks out in contaminated areas, and carelessness can result in the ingestion of asbestos.
OTHER CANCERS

## Slide 32
Amount of fibers inhaled
Length of exposure
Whether exposed worker smokes
Age – because of delayed effects
The potential for asbestos related disease depends on:
Don’t smoke! An asbestos worker is at much greater risk of developing lung cancer if he/she smokes.
ASBESTOS-RELATED DISEASES
Smoking cessation program information available and provided by employers.

## Slide 33
THE DANGERS OF ASBESTOS
What you need to know:
Removal or disturbing of asbestos containing material is very dangers
Can release large amounts into the air
Very small amounts can cause chronic effects in all people exposed
Workers can bring the contaminated dust home and poison their families
Non-friable ACM (floor and ceiling tiles, house siding, fire doors, etc.) won’t release fibers unless disturbed or damaged in some way.

## Slide 34
DANGER: LEAD

## Slide 35
LEAD DEFINITION
LEAD:
Lead is a highly toxic metal
Found in many common materials including:
      old paints and primers
      industrial paints
      car batteries
      bullets
      electronics
Materials containing lead are often encountered during construction maintenance and manufacturing
Notes: Lead:
Lead is a highly toxic metal (element named Pb) that’s found in many common materials including old paints and primers, industrial paints and primers, car batteries, bullets, and electronics. Materials containing lead are often encountered during construction, maintenance, and manufacturing activities.

## Slide 36
LEAD INFORMATION
Why was lead used in paint?
      Lead was added for color and durability
      Lead-based paint was banned in 1978
Notes: What you need to know about lead:
Working with products with lead can expose expose workers to lead, especially during renovations that disturb paint with lead based paint.
Lead-contaminated dust is poisonous.
Very small amounts of lead-contaminated dust can poison workers (inhalation or ingestion).
Workers can take home dust that poisons their families.

## Slide 37
How Much Lead Matters?
ANY lead-containing material at a job site is dangerous to workers!
Labor and Industries regulates any level of exposure to workers.
The Permissible Exposure Limit (PEL) for lead in construction is:
    50 μg/m3 per 8 hour Time Weighted Average (TWA).
THE DANGERS OF LEAD
WAC 296-155-17607 (1)
Notes: How Much Lead Matters?
Any lead containing material at a job site is dangerous to workers and is regulated by Labor and Industries.
The Permissible Exposure Limit (PEL) for lead in construction is:
50 μg/m3 per 8 hour Time Weighted Average (TWA).
Lead is often found in paint in pre-1978 houses. EPA defines Lead Based Paint (LBP) as :
Any paint or surface coatings that contain lead equal to or in excess of 1.0 milligram per square centimeter or more than 0.5 percent by weight.
For a visual example of 1 mg, an Equal Packet is about 1 Gram (.035 oz) or 15,543 Grains.
A milligram is 1/1000 of a gram or about 15 grains. A microgram (μg) is 1/1,000,000 of a gram or about .015 grains.
Lead is also found in: Lead pipes and plumbing
Roof Flashing
Leaded Gasoline and Jet Fuel
Radiator repair
Battery handling
Lead Casting
Welding
Bridge and Marine Work
Actionable Blood Lead Levels (BLL)
50 μg/dL - workers removed from job 20 μg/dL - CDC recommends children removed from home 5 μg/dL - level of concern
If workers, adults, or children are found with lead in their blood, it is likely they have ingested or inhaled it within the last 6-8 weeks. Studies show over 1/2 of lead ‘poisonings’ happen after renovation work involving LBP. Lead will do its damage while in the blood stream and either be excreted or absorb into bones.

## Slide 38
THE DANGERS OF LEAD
EPA/COMMERCE standards define lead-based paint as:
    Any paint or surface coatings that contain lead equal to or in excess of 1.0 milligram per square centimeter or more than 0.5 percent by weight
    It is the primary source of lead-contaminated dust in housing
15,543 Grains in a Gram
Milligram (mg) = 15 grains
Microgram (μg) = .15 (50 μg is .77 of a grain)
Notes: When dealing with particulate health hazards, it only takes a small amount to do big damage. To get a mental picture.

## Slide 39
HEALTH EFFECTS
Hazardous to Workers:
brain damage
loss of sex drive and male infertility
physical fatigue
nervous system disorders
digestive problems
memory or concentration problems
muscle and joint pain
kidney damage
blood effects
acute toxicity effects
WAC 296-155-17625 (1)(a)
Notes: Route of Entry:
Though it causes no harm when undisturbed, when inhaled or ingested as a dust it can cause severe health effects in workers, children, and pregnant women.
Lead distributes throughout the body in the blood and is accumulated in the bones and can adversely affect the nervous system, kidney function, immune system, reproductive and developmental systems and the cardiovascular system.
Health Effects:
Hazardous to Workers
Brain Damage
Reduction in the blood’s ability to carry oxygen.
Loss of sex drive and/or capability.
Male Infertility
Physical fatigue.
Nervous System Disorders
Digestive Problems
Memory or Concentration Problems
Muscle and Joint Pain
Very hazardous to children
Damages the brain and central nervous system; can cause decreased intelligence, reading and learning difficulties, behavioral problems, and hyperactivity.
Children under 6 are especially susceptible to permanent brain damage from lead
Hazardous to pregnant women
Damage to the fetus.
Miscarriages can be due to lead exposure by partner

## Slide 40
THE DANGERS OF LEAD
VERY Hazardous to Children:
damages the brain and central nervous system
causes decreased intelligence, reading and learning disabilities
behavioral problems and hyperactivity
children under 6 are especially susceptible to permanent brain damage
Hazardous to Pregnant Women:
damage to the fetus
miscarriages can be due to lead exposure of parter
WAC 296-155-17625 (1)(a)
Notes: Route of Entry:
Though it causes no harm when undisturbed, when inhaled or ingested as a dust it can cause severe health effects in workers, children, and pregnant women.
Lead distributes throughout the body in the blood and is accumulated in the bones and can adversely affect the nervous system, kidney function, immune system, reproductive and developmental systems and the cardiovascular system.
Health Effects:
Hazardous to Workers
Brain Damage
Reduction in the blood’s ability to carry oxygen.
Loss of sex drive and/or capability.
Male Infertility
Physical fatigue.
Nervous System Disorders
Digestive Problems
Memory or Concentration Problems
Muscle and Joint Pain
Very hazardous to children
Damages the brain and central nervous system; can cause decreased intelligence, reading and learning difficulties, behavioral problems, and hyperactivity.
Children under 6 are especially susceptible to permanent brain damage from lead
Hazardous to pregnant women
Damage to the fetus.
Miscarriages can be due to lead exposure by partner
Appendix A to WAC 296-155-176:
Ways in which lead enters your body. When absorbed into your body in certain doses, lead is a toxic substance. The object of the lead standard is to prevent absorption of harmful quantities of lead. The standard is intended to protect you not only from the immediate toxic effects of lead, but also from the serious toxic effects that may not become apparent until years of exposure have passed. Lead can be absorbed into your body by inhalation (breathing) and ingestion (eating). Lead (except for certain organic lead compounds not covered by the standard, such as tetraethyl lead) is not absorbed through your skin. When lead is scattered in the air as a dust, fume respiratory tract. Inhalation of airborne lead is generally the most important source of occupational lead absorption. You can also absorb lead through your digestive system if lead gets into your mouth and is swallowed. If you handle food, cigarettes, chewing tobacco, or make-up which have lead on them or handle them with hands contaminated with lead, this will contribute to ingestion. A significant portion of the lead that you inhale or ingest gets into your blood stream. Once in your blood stream, lead is circulated throughout your body and stored in various organs and body tissues. Some of this lead is quickly filtered out of your body and excreted, but some remains in the blood and other tissues. As exposure to lead continues, the amount stored in your body will increase if you are absorbing more lead than your body is excreting. Even though you may not be aware of any immediate symptoms of disease, this lead stored in your tissues can be slowly causing irreversible damage, first to individual cells, then to your organs and whole body systems.

## Slide 41
THE DANGERS OF LEAD
What you need to know:
Renovations can make dust and debris that has lead in it.
Lead-contaminated dust is poisonous!!
Very small amounts of this dust can poison workers.
When this dust is inhaled or ingested the lead distributes throughout the body in the blood and causes long term health effects
Workers can take home dust that poisons their families.
Notes: What you need to know about lead:
Working with products with lead can expose expose workers to lead, especially during renovations that disturb paint with lead based paint.
Lead-contaminated dust is poisonous.
Very small amounts of lead-contaminated dust can poison workers (inhalation or ingestion).
Workers can take home dust that poisons their families.

## Slide 42
DANGER: SILICA

## Slide 43
THE DANGERS OF SILICA
Crystalline silica is a material found in the earth’s crust - a mineral that occurs in several forms
Quartz - the most common form - is a component of many construction materials including:
Notes: Silica:
Crystalline silica is an important industrial material found abundantly in the earth’s crust. It is a mineral that occurs in several forms. Quartz, the most common form, is a component of sand, stone, rock, concrete, brick, block, and mortar, and sand used for blasting. Other construction materials that contain crystalline silica are asphalt filler, roofing granules, plastic composites, soils, and to a lesser extent, some wallboard joint compounds, paint, plaster, caulking and putty.

## Slide 44
THE DANGERS OF SILICA
SILICA IS FOUND:
stone
rock
concrete
brick
block
mortar
sand used for blasting
asphalt filler
roofing granules
plastic composites
Notes: Silica:
Crystalline silica is an important industrial material found abundantly in the earth’s crust. It is a mineral that occurs in several forms. Quartz, the most common form, is a component of sand, stone, rock, concrete, brick, block, and mortar, and sand used for blasting. Other construction materials that contain crystalline silica are asphalt filler, roofing granules, plastic composites, soils, and to a lesser extent, some wallboard joint compounds, paint, plaster, caulking and putty.

## Slide 45
THE DANGERS OF SILICA
Health Effects:
Diseases caused by occupation Silica exposure:
Silicosis - a serious and fatal lung disease
Chronic Obstructive Pulmonary Disease
Bronchitis and Emphysema
Also causes: extreme shortness of breath, chest pain, respiratory failure and death
There is no cure!
Route of Entry: :Tiny respirable-sized particles (that can get into the deep lung) are not visible
Once in the lung, the jagged particles are surrounded by scar tissue, the body’s defense
Notes: Route of Entry:
Visible dust contains large particles that are easy to see. The tiny, respirable-sized particles (those that can get into the deep lung) containing silica pose the greatest hazard and are not visible. Once in the lung, the jagged particles are surrounded by the bodies defense system which causes lungs to fill with unremovable solid material or scar tissue.
Health Effects:
Occupational exposure to respirable crystalline silica has been shown to cause silicosis, a serious and sometimes fatal lung disease. It is also associated with chronic obstructive pulmonary disease, including bronchitis and emphysema. The results of some epidemiologic studies suggest that these diseases may be less frequent or absent in nonsmokers.
Long term effects include extreme shortness of breath, chest pain, respiratory failure and death.

## Slide 46
THE DANGERS OF SILICA
What you need to know:
Visible dust means you are being exposed to high levels of respirable dust and are way over the PEL
Include air monitoring in your plan and provide respirators when control methods cannot limit exposure
Notes: What you need to know about silica:
Visible dust while cutting concrete, block, rock, granite, or while sandblasting is an indication you are being exposed to high levels of respirable dust, much over the PELs.
Measures that control tool-generated dust at the source usually reduce all types of particle emissions, including respirable particles.
Engineering controls include such measures as local exhaust ventilation, wet methods, and high efficient particulate air (HEPA) vacuums and attachments are the safest way to protect workers and reduce exposure.
Simply limiting workers' access to areas where they could be exposed above the PEL is a valuable protection method.
Include air monitoring in your overall plan and provide respirators to workers when dust controls cannot limit exposures to the PEL,

## Slide 47
THE DANGERS OF SILICA
How Much Silica Matters?
Crystaline Quartz Silica has a PEL of 0.1 mg/m3 and a STEL of 0.3 mg/m3.
  You must protect workers from silica dust exposure in all its forms
Proposed OSHA Silica Rules:
OSHA is reviewing the construction and general industry PELs for silica in its ongoing rule making.
Notes: Proposed OSHA Silica Rules
OSHA is reviewing the construction and general industry PELs for silica in its ongoing silica rulemaking. The new proposed rule by OSHA is 50 μg/m3. for all industries and types of Silica. It will also include an ‘action level’ of 25 μg/m3 that requires employers to institute protective measures. Labor and Industries will be required to adopt the new levels if passed by OSHA. The rules will also require medical exams for employees who work with silica.
a medical and work history,
physical examination with
(3) a chest X-ray
(4) a pulmonary function test administered by spirometry technician
(5) testing for latent tuberculosis
(6) other tests deemed appropriate by the physician or licensed health care
professional (PLHCP).

## Slide 48
AT RISK WORKERS
Cement siding installers
Concrete, block, or cement cutting
Granite Counter Top Installers
Concrete, fill, or leveling product mixers (pouring bags by hand)
Abrasive Blasters
Drywall Finishers
Heavy Equipment Operators
Hole Drillers using hand-held drills
Rock-crushing machine operators
Tuckpointers and Grinders
Underground Construction
Masonry Cutters - Portable and Stationary Saws
Millers
Rock and concrete drillers
Jackhammer and Impact Drillers
CONSTRUCTION ACTIVITIES AFFECTED BY SILICA:

## Slide 49
DANGER: MOLD

## Slide 50
THE DANGERS OF MOLD
MOLD:
Molds are microscopic organisms found everywhere in the environment, indoors and outdoors
Mold is a type of fungi
Most molds reproduce by forming spores that are released into the air, land on a moist surface, begin to grown, penetrate proud materials and release chemicals
Notes: Mold:
Molds are microscopic organisms found everywhere in the
environment, indoors and outdoors. Mold is a type of fungi. Most molds reproduce by forming spores which are released into the air. When spores land on a suitable moist surface they begin to grow, can penetrate porous materials and release chemicals. Buildings with significant moisture build up are the most susceptible to having molds grow. In residences, moisture can be caused by leaks, cooking practices, and even overwatering of plants.

## Slide 51
How Much Mold Matters?
There are no current specific regulation on mold in the workplace
WAC 296-841-100 required an exposure assessment of airborne contaminates including harmful bacteria or fungi
If you can smell or see mold, there is a potential health risk
Testing for Mold:
Testing for mold is varied and subjective, and no safe standard has been established
End-of-project testing should show that the levels and types of mold present are similar to those found outside the building
THE DANGERS OF MOLD
Notes: How Much Mold Matters?
There are no current specific regulations on mold in the workplace. But the ‘general duty’ or ‘management responsibility’ clause of WAC 296-841-100 requires an exposure assessment of airborne contaminants, including harmful bacteria or fungi. This would include motivate employers to protect their workers from mold.
If mold is seen or smelled, there is a potential health risk; therefore, no matter what type of mold is present, you should arrange for its removal.
Testing for mold is varied and subjective, and no safe standard is established. Generally, end of project testing should show that the level and types of mold and mold spores inside the building are similar to those found outside.
Note: Regulated materials, such as lead or asbestos, require specific mitigation and remediation protocols. The presence of these and other regulated materials take precedence over mold remediation, and they shall be addressed according to applicable federal, state, provincial and local laws and regulations.
Many industries base their mold remediation techniques on EPA recommendations or some States have adopted the (Institute of Inspection Cleaning and Restoration Certification) IICRC 520-2008 standard on mold remediation.

## Slide 52
THE DANGERS OF MOLD
Route of Entry: :
Inhalation is the most common exposure
Workers can be exposed to mold:
    during demolition
    during mold remediation (complete removal)
    construction activities when mold spores are released into the air in construction dust
Notes: Route of Entry:
Inhalation is the exposure of most concern to cleanup workers who are exposed to mold during demolition, mold remediation, or construction activities when mold spores are aerosolized or released into the air in construction dust.
Health Effects:
Most molds are harmless but some can cause infections, allergy symptoms, produce toxins, and release volatile organic compounds.
Research studies have linked mold to respiratory symptoms, asthma, hypersensitivity pneumonitis, bronchitis, and related respiratory infections. In addition, exposure to mold can irritate the eyes, skin, nose and throat in certain individuals. The onset of symptoms and reactions to mold can be either immediate or delayed.

## Slide 53
THE DANGERS OF MOLD
Health Effects:
Some mold can cause infections, allergy symptoms, produce toxins and release volatile organic compounds
Mold has been linked to asthma, hypersensitivity pneumonitis, bronchitis and respiratory infection
The onset of symptoms and reactions can be immediate or delayed
Notes: Route of Entry:
Inhalation is the exposure of most concern to cleanup workers who are exposed to mold during demolition, mold remediation, or construction activities when mold spores are aerosolized or released into the air in construction dust.
Health Effects:
Most molds are harmless but some can cause infections, allergy symptoms, produce toxins, and release volatile organic compounds.
Research studies have linked mold to respiratory symptoms, asthma, hypersensitivity pneumonitis, bronchitis, and related respiratory infections. In addition, exposure to mold can irritate the eyes, skin, nose and throat in certain individuals. The onset of symptoms and reactions to mold can be either immediate or delayed.

## Slide 54
What you need to know:
The idea that you can “kill mold” with bleach does not fit modern mold research or industry standards
Identify and stop leaks and moisture sources to control the problem long term
Contain the area - Do not let mold spores spread to uncontaminated areas.
THE DANGERS OF MOLD
Notes: What you need to know about mold:
The idea that you can just “kill mold” with some bleach does not fit modern mold research or construction industry standards.
Identify and stop the leaks and moisture sources in the building. Stop the cause of mold growth to control the problem long term.
Contain area where mold remediation will be occurring, do not let mold spores spread to uncontaminated areas. Containment procedures are discussed later in the handout.
Negative air machines should be used to vent contained areas to the outside of the building through HEPA filtration devices.
Physically removing visible mold, mold-damaged materials, is the preferred method of mold remediation. Remove materials in as large of pieces as possible to prevent dust. Use damp (minimal wetness) methods while removing materials.
Antimicrobials and Biocides should only be used by trained professionals and application must meet government regulation standards for use, including application and disposal requirements. Killing mold spores does not stop the destroy their antigenic or toxigenic properties.
Proper cleanup, including HEPA vacuuming and damp wiping of all surfaces is required to reduce the chances of re-contamination of mold in the remediated area.

## Slide 55
What you need to know:
Use negative air machines to vent the contained areas through HEPA filtration device
Completely remove visible mold and mold-damage materials
Antimicrobials and Biocides should only be used by trained professionals
Proper cleanup, including HEPA vacuuming is required to reduce the chances of recontamination
THE DANGERS OF MOLD
Notes: What you need to know about mold:
The idea that you can just “kill mold” with some bleach does not fit modern mold research or construction industry standards.
Identify and stop the leaks and moisture sources in the building. Stop the cause of mold growth to control the problem long term.
Contain area where mold remediation will be occurring, do not let mold spores spread to uncontaminated areas. Containment procedures are discussed later in the handout.
Negative air machines should be used to vent contained areas to the outside of the building through HEPA filtration devices.
Physically removing visible mold, mold-damaged materials, is the preferred method of mold remediation. Remove materials in as large of pieces as possible to prevent dust. Use damp (minimal wetness) methods while removing materials.
Antimicrobials and Biocides should only be used by trained professionals and application must meet government regulation standards for use, including application and disposal requirements. Killing mold spores does not stop the destroy their antigenic or toxigenic properties.
Proper cleanup, including HEPA vacuuming and damp wiping of all surfaces is required to reduce the chances of re-contamination of mold in the remediated area.