## Slide 1
LEAD, ASBESTOS, SILICA, & MOLD
PART 2
Funding and support for this project provided by State of Washington, Department of Labor and Industries, Safety and Health Investments projects.
HEALTH HAZARDS
IN CONSTRUCTION

## Slide 2
REGULATIONS: ABSBESTOS

## Slide 3
AGENCIES REGULATING ASBESTOS
EPA
ENVIRONMENTAL
40 CFR 763 / 40 CFR 61
OSHA (D.O.L)
WORKER SAFETY 29 CFR 1926.1101
AHERA ASHARA NESHAP
LABOR AND INDUSTRIES
DEPARTMENT OF SAFETY AND HEALTH (DOSH)
FEDERAL DEPARTMENTS
WASHINGTON STATE ENFORCEMENT
WA DEPT OF ECOLOGY
LOCAL CLEAN AIR AUTHORITY
ASBESTOS
WAC 296-62-077
SAFETY STANDARDS FOR ASBESTOS REMOVAL & ENCAPSULATION WAC 296-65

## Slide 4
REGULATIONS FOR ASBESTOS
Asbestos “Good Faith” Surveys
  Required on all renovations to determine if it is an Asbestos Project
  Completed by an AHERA Building Inspector
  Results of the survey must be shared with any contractor on the job site
  L&I can impose a minimum $250/day fine for not having a survey
  Local clean air authority $1000s
REQUIRED ALL RENOVATIONS/ ALL CONTRACORS
Notes: ASBESTOS SURVEYS REQUIRED ON ALL RENOVATIONS:
Before starting a renovation of any public or private building, regardless of the year built, Building Owners are required to obtain a written asbestos survey completed by an AHERA Building Inspector.
Results of the survey must be shared with any Contractor performing work, so they can determine if their workers will be exposed to Asbestos Containing Materials.
Labor and Industries Fines
L&I can impose a minimum $250 per day fine for failure to obtain an asbestos survey. This fine can be applied to both the contractor and building owner. Additional fines may be applied if employers are not complying with all applicable safety and health standards.
More Information at:
http://www.lni.wa.gov/TradesLicensing/LicensingReq/Asbestos/default.asp#1
EVEN MORE REGULATIONS:
AHERA/ASHARA Asbestos Hazard and Emergency Response Act & Asbestos School Hazards Abatement Reauthorization Act 40 CFR 763:
Mandated identifying Asbestos Containing Materials in Schools
ASHARA defined Asbestos projects regulations in all Public buildings
NESHAP National Emission Standards for Hazardous Air Pollutants (NESHAP) 40 CFR Part 61, Subpart M
AHERA Accredited Inspections for buildings are required in some jurisdictions by Department of Ecology recognized local clean air authority. For more information: http://www.ecy.wa.gov/programs/air/local.html

## Slide 5
REGULATIONS FOR ASBESTOS
Asbestos Awareness:
  All employees that may come into contact with asbestos must attend a 2-hour Asbestos Awareness course covering identification and dangers of asbestos
  This course does not entitle you to do any asbestos related work!
Notes: ASBESTOS AWARENESS:
All employees that that may come into contact with asbestos or presumed asbestos containing material must attend a two (2) hour Asbestos Awareness course, covering the identification and dangers of asbestos. | This course DOES NOT ENTITLE YOU TO DO ANY ASBESTOS RELATED WORK. Asbestos related work is fully regulated by class of work and requires a Contractors Registration, Asbestos Contractor Certification, accredited training, and specific equipment mandated by WAC 296-62-077 and WAC 296-65.
ASBESTOS ABATEMENT/DEMOLITION PROJECTS REQUIRE:
Registered Contractors must be certified as an Asbestos Contractor with Labor and Industries (annual renewal)
Notification 10 Day Prior to Work Starting to Labor and Industries for Asbestos Projects over 48 sq2 or with more than 10 lnft of pipe.
Notification 10 Day Prior to Work Starting to local Clean Air Authority for Asbestos Projects over 48 sq2 or with more than 10 lnft of pipe.
Buildings Surveyed by an AHERA Building Inspector (3 Day Training for Inspector’s Required with an Annual Refresher): Can perform inspections and clearance testing.
Asbestos Supervisor (40 hour required Class, Annual Refresher): Supervise asbestos workers and required on all asbestos projects.
Asbestos Worker (32 hour required class, Annual Refresher): Perform abatement and encapsulation activities under the direction of an Asbestos Supervisor.
Optional Specific Trade Asbestos Worker (Certified Asbestos contractors can utilized workers for specific work who have had 8 hour of training specific to one category of asbestos containing material, examples include flooring, roofing, or cleaning and maintenance).
ASBESTOS CLASSES OF WORK:
Class I asbestos work means activities involving the removal of thermal system insulation or surfacing ACM/PACM.
Class II asbestos work means activities involving the removal of ACM which is not thermal system insulation or surfacing material. This includes, but is not limited to, the removal of asbestos-containing wallboard, floor tile and sheeting, roofing and siding shingles, and construction mastics.
Class III asbestos work means repair and maintenance operations where "ACM," including TSI and surfacing ACM and PACM, may be disturbed.
Class IV asbestos work means maintenance and custodial activities during which employees contact but do not disturb ACM or PACM and activities to clean up dust, waste and debris resulting from Class I, II, and III activities.

## Slide 6
REGULATIONS FOR ASBESTOS
What is an “Asbestos Project” ?
Includes the construction, demolition, repair, remodeling, maintenance or renovation of any public or private building or structure, mechanical piping equipment or system involving the demolition, removal, encapsulation, salvage, or disposal of material or outdoor activity releasing or likely to release asbestos fibers into the air.
Agencies that Regulate Asbestos in WA State:
Labor and Industries
Dept of Ecology - Local Clean Air Authorities
FOR ASBESTOS CONTRACTORS ONLY!!

## Slide 7
REGULATIONS FOR ASBESTOS
Asbestos Abatement/Demolition Projects Require:
Contractors must be certified as an Asbestos Contractor with Labor and Industries
Must have an Asbestos Supervisor on Staff
Must use Asbestos Workers or Optional Specific trade workers
Must notify if project is greater than 48 soft or 10 lnft
Notification 10 days prior to work starting to L&I
Notification 10 days prior to work to local Clean Air Authority
Notes: ASBESTOS AWARENESS:
All employees that that may come into contact with asbestos or presumed asbestos containing material must attend a two (2) hour Asbestos Awareness course, covering the identification and dangers of asbestos. | This course DOES NOT ENTITLE YOU TO DO ANY ASBESTOS RELATED WORK. Asbestos related work is fully regulated by class of work and requires a Contractors Registration, Asbestos Contractor Certification, accredited training, and specific equipment mandated by WAC 296-62-077 and WAC 296-65.
ASBESTOS ABATEMENT/DEMOLITION PROJECTS REQUIRE:
Registered Contractors must be certified as an Asbestos Contractor with Labor and Industries (annual renewal)
Notification 10 Day Prior to Work Starting to Labor and Industries for Asbestos Projects over 48 sq2 or with more than 10 lnft of pipe.
Notification 10 Day Prior to Work Starting to local Clean Air Authority for Asbestos Projects over 48 sq2 or with more than 10 lnft of pipe.
Buildings Surveyed by an AHERA Building Inspector (3 Day Training for Inspector’s Required with an Annual Refresher): Can perform inspections and clearance testing.
Asbestos Supervisor (40 hour required Class, Annual Refresher): Supervise asbestos workers and required on all asbestos projects.
Asbestos Worker (32 hour required class, Annual Refresher): Perform abatement and encapsulation activities under the direction of an Asbestos Supervisor.
Optional Specific Trade Asbestos Worker (Certified Asbestos contractors can utilized workers for specific work who have had 8 hour of training specific to one category of asbestos containing material, examples include flooring, roofing, or cleaning and maintenance).
ASBESTOS CLASSES OF WORK:
Class I asbestos work means activities involving the removal of thermal system insulation or surfacing ACM/PACM.
Class II asbestos work means activities involving the removal of ACM which is not thermal system insulation or surfacing material. This includes, but is not limited to, the removal of asbestos-containing wallboard, floor tile and sheeting, roofing and siding shingles, and construction mastics.
Class III asbestos work means repair and maintenance operations where "ACM," including TSI and surfacing ACM and PACM, may be disturbed.
Class IV asbestos work means maintenance and custodial activities during which employees contact but do not disturb ACM or PACM and activities to clean up dust, waste and debris resulting from Class I, II, and III activities.

## Slide 8
REGULATIONS FOR ASBESTOS
Even more regulations for Schools and Public Buildings:
AHERA Asbestos Hazard and Emergency Response Act
AHSARA Asbestos School Hazards Abatement Reauthorization Act
NESHAP National Emission Standards for Hazardous Air Pollutants
Notes: ASBESTOS AWARENESS:
All employees that that may come into contact with asbestos or presumed asbestos containing material must attend a two (2) hour Asbestos Awareness course, covering the identification and dangers of asbestos. | This course DOES NOT ENTITLE YOU TO DO ANY ASBESTOS RELATED WORK. Asbestos related work is fully regulated by class of work and requires a Contractors Registration, Asbestos Contractor Certification, accredited training, and specific equipment mandated by WAC 296-62-077 and WAC 296-65.
ASBESTOS ABATEMENT/DEMOLITION PROJECTS REQUIRE:
Registered Contractors must be certified as an Asbestos Contractor with Labor and Industries (annual renewal)
Notification 10 Day Prior to Work Starting to Labor and Industries for Asbestos Projects over 48 sq2 or with more than 10 lnft of pipe.
Notification 10 Day Prior to Work Starting to local Clean Air Authority for Asbestos Projects over 48 sq2 or with more than 10 lnft of pipe.
Buildings Surveyed by an AHERA Building Inspector (3 Day Training for Inspector’s Required with an Annual Refresher): Can perform inspections and clearance testing.
Asbestos Supervisor (40 hour required Class, Annual Refresher): Supervise asbestos workers and required on all asbestos projects.
Asbestos Worker (32 hour required class, Annual Refresher): Perform abatement and encapsulation activities under the direction of an Asbestos Supervisor.
Optional Specific Trade Asbestos Worker (Certified Asbestos contractors can utilized workers for specific work who have had 8 hour of training specific to one category of asbestos containing material, examples include flooring, roofing, or cleaning and maintenance).
ASBESTOS CLASSES OF WORK:
Class I asbestos work means activities involving the removal of thermal system insulation or surfacing ACM/PACM.
Class II asbestos work means activities involving the removal of ACM which is not thermal system insulation or surfacing material. This includes, but is not limited to, the removal of asbestos-containing wallboard, floor tile and sheeting, roofing and siding shingles, and construction mastics.
Class III asbestos work means repair and maintenance operations where "ACM," including TSI and surfacing ACM and PACM, may be disturbed.
Class IV asbestos work means maintenance and custodial activities during which employees contact but do not disturb ACM or PACM and activities to clean up dust, waste and debris resulting from Class I, II, and III activities.

## Slide 9
ASBESTOS CLASSES OF WORK:
Class I asbestos work means activities involving the removal of thermal system insulation or surfacing ACM/PACM.
Class II asbestos work means activities involving the removal of ACM which is not thermal system insulation or surfacing material. This includes, but is not limited to, the removal of asbestos-containing wallboard, floor tile and sheeting, roofing and siding shingles, and construction mastics.
Class III asbestos work means repair and maintenance operations where "ACM," including TSI and surfacing ACM and PACM, may be disturbed.
Class IV asbestos work means maintenance and custodial activities during which employees contact but do not disturb ACM or PACM and activities to clean up dust, waste and debris resulting from Class I, II, and III activities.
REGULATIONS FOR ASBESTOS

## Slide 10
REGULATIONS FOR ASBESTOS
Asbestos Abatement Contractors must have a Medical Surveillance Program:
  For all employees exposed to airborne concentrations of asbestos fibers at or above the PEL
  Includes pulmonary function test, chest roentgenogram, examination of all cardiovascular and gastrointestinal systems
  Yearly Checkups

## Slide 11
REGULATIONS: LEAD

## Slide 12
EPA
ENVIRONMENTAL
40 CFR 745
HUD
HOUSING
24 CFR 35
OSHA (D.O.L)
WORKER SAFETY 29 CFR 1926.62
RENOVATION, REPAIR, AND PAINTING (RRP)
WAC 365-230
LABOR AND INDUSTRIES
DEPARTMENT OF SAFETY AND HEALTH (DOSH)
FEDERAL DEPARTMENTS
WASHINGTON STATE ENFORCEMENT
AGENCIES REGULATING LEAD
WA DEPT OF COMMERCE
WA DEPT OF COMMERCE
LEAD SAFE HOUSING RULE WAC 365-230
LEAD IN CONSTRUCTION
WAC 296-155-176

## Slide 13
REGULATIONS FOR LEAD WORKER SAFETY - LABOR AND INDUSTRIES
Worker Safety Rules
WAC 296-155-176 standard applies to workers when they work with any presumed or actual lead containing material at any level.
If employees are exposed to lead in any form, the companies are required to have a:
Competent Person Training
Written Compliance Plan for Lead in Construction
Air Monitoring
Appropriate Personal Protective Equipment
Decontamination
Designated Eating Areas
Respiratory Protection Program
Notes: WORKER SAFETY RULES - LEAD
WAC 296-155-176 standard applies to workers when they work with any presumed or actual lead containing material at any level.
There is no difference in the worker requirements between doing “abatement” work or “renovation” work when it comes to following the Lead in Construction Standard.
Companies are required to have a :
WRITTEN COMPLIANCE PLAN FOR LEAD IN CONSTRUCTION updated every 6 months, that covers your companies plan for:
Company COMPETENT PERSON Training requirements
A description of each activity in which lead is emitted;
A description of the specific means to achieve compliance in keeping workers
A report of the technology considered in meeting the PEL
Air monitoring data which documents the source of lead emissions
A detailed schedule for implementation of the program,
A work practice program
An administrative control schedule, if applicable
Inspections of job sites, materials, and equipment to be made by a competent person
OTHER REQUIREMENTS
Air Monitoring
Initial air monitoring for exposure
Assumed exposure levels
PPE Requirements
Respirator per WAC 296-842
Coveralls, goggles, head and hand protection
Decontamination requirements
change room, hand washing facility
showers where feasible
Designated Eating Areas
Respiratory Protection Program

## Slide 14
REGULATIONS FOR LEAD
Lead in Construction’ Rule Requires Training for Workers:
The employer shall provide the training program as initial training prior to the time
The employer shall also at least annually for each employee
The content of WAC 296-155-176 and its appendices (provide links to website)
Training regarding the specific nature of the operation and work practices, PPE, housekeeping, and related plans
REGULATIONS FOR LEAD RENOVATION
WAC 296-155-17625 (2)(a) and (b)
Notes: LABOR AND INDUSTRIES ‘LEAD IN CONSTRUCTION’ RULE REQUIRES TRAINING FOR WORKERS:
Workers who are exposed to the action level of lead are required to get initial training on the following information and then at least annually after. No specific hour requirement is listed, but training must include:
The content of WAC 296-155-176 and its appendices;
The work practices which could result in exposure to lead above the action level;
Respiratory protection per WAC 296-842.
Medical Evaluations
Fit Testing
The purpose and a description of the companies medical surveillance program, and the medical removal protection program which requires:
The adverse health effects associated with excessive exposure to lead (with particular attention to the adverse reproductive effects on both males and females and hazards to the fetus and additional precautions for employees who are pregnant);
Initial Baseline Blood Lead Level (BLL) and Zinc Protoporphyrin Levels (ZPP) Test
At least every two months for the first six months and every six months thereafter for employees who are or may be exposed by the employer at or above the action level for more than thirty days in any consecutive twelve months;
Follow up every 60 days for workers with a BLL > 40 μg/dL
Instructions to employees that chelating agents should not routinely be used to remove lead from their bodies and should not be used at all except under the direction of a licensed physician
Employee must have temporary removal from work place due to elevated blood lead level. The employer shall remove an employee from work having an exposure to lead at or above the action level on each occasion that a periodic and a follow-up blood sampling test conducted pursuant to WAC 296-155-176 indicate that the employee's blood lead level is at or above 50 µg/dl; and return when below 40 µg/dl.
Hazard Communication Training
The engineering controls and work practices associated with the employee's job assignment (Appendix B, WAC 296-155-17652)
The contents of any compliance plan in effect;
The employee's right of access to records
The employer shall make readily available to all affected employees a copy of this standard and its appendices.
The employer shall provide, upon request, all materials relating to the employee information and training program to affected employees and their designated representatives, and the director.

## Slide 15
TRIGGER TASKS IN RENOVATIONS CONSTRUCTION | TRAINING REQUIRED | AIR MONITORING | PERSONAL PROTECTIVE EQUIPMENT | DECONTAMINATION
296-155-176 (2)(a)(i) The tasks covered by this requirement are: Manual demolition of structure, manual scraping, heat gun applications, power tools with dust collection (DISTURBING LEAD BASED PAINT UNDER THE RRP) (ii) spray painting with lead paint or (b) employer has any reason to believe worker performing a task may be exposed over the PEL | WAC 296-155-17625 Lead in Construction Program WAC 296-901-140, Hazard communication; WAC 296-155-17625 Respirator Program; WAC 296-155-100 Accident Prevention Program | Until the employer performs an employee exposure assessment, the employer shall treat the employee as if the employee were exposed above the PEL, and not in excess of ten (10) times the PEL. | Appropriate respiratory protection in accordance with WAC 296-155-17613. 1/2 Mask Respirator with P100 Filters (ii) Appropriate personal protective clothing and equipment in accordance with WAC 296-155-17615. Disposable Coveralls or full body work clothing. Gloves, hats, and disposable shoe covers Face Shields or vented goggles. | (iii) Change areas in accordance with WAC 296-155-17619(2). (iv) Hand washing facilities in accordance with WAC 296-155-17619(5).
NATURE OF OPERATIONS
RENOVATION
WAC 296-155-17625 (2)(b) and (e)

## Slide 16
TRIGGER TASKS IN RENOVATIONS CONSTRUCTION | TRAINING REQUIRED | AIR MONITORING | PERSONAL PROTECTIVE EQUIPMENT | DECONTAMINATION
296-155-176 (2)(c) The tasks covered by this requirement are: (i) Using lead containing mortar; lead burning; (ii) Where lead containing coatings or paint are present: Rivet busting; power tool cleaning without dust collection systems; cleanup activities where dry expendable abrasives are used; and abrasive blasting enclosure movement and removal. | WAC 296-155-17625 Lead in Construction Program WAC 296-901-140, Hazard communication; WAC 296-155-17625 Respirator Program; WAC 296-155-100 Accident Prevention Program | Exposure Monitoring Required Until such assessment the Employer assumes the exposure is above 500 mg/m3` | Appropriate respiratory protection in accordance with WAC 296-155-17613. Full Face Respirator with P100 Filters (ii) Appropriate personal protective clothing and equipment in accordance with WAC 296-155-17615. Disposable Coveralls or full body work clothing. Gloves, hats, and disposable shoe covers. | (iii) Change areas in accordance with WAC 296-155-17619(2). (iv) Hand washing facilities in accordance with WAC 296-155-17619(5)
NATURE OF OPERATIONS
RENOVATION
WAC 296-155-17625 (2)(b) and (e)

## Slide 17
TRIGGER TASKS IN RENOVATIONS CONSTRUCTION | TRAINING REQUIRED | AIR MONITORING | PERSONAL PROTECTIVE EQUIPMENT | DECONTAMINATION
296-155-176 (2)(c) Protection described in this section is required where lead containing coatings or paint are present on structures when performing: (i) Abrasive blasting; (ii) Welding; (iii) Cutting; and (iv) Torch burning. | WAC 296-155-17625 Lead in Construction Program WAC 296-901-140, Hazard communication; WAC 296-155-17625 Respirator Program; WAC 296-155-100 Accident Prevention Program | Exposure Monitoring Required Until such assessment the Employer assumes the employee were exposed to lead in excess of 2,500 µg/m3 | Appropriate respiratory protection in accordance with WAC 296-155-17613. Supplied Air Respirator with Grade D Air (ii) Appropriate personal protective clothing and equipment in accordance with WAC 296-155-17615. Disposable Coveralls or full body work clothing. Gloves, hats, and disposable shoe covers. | (iii) Change areas in accordance with WAC 296-155-17619(2). (iv) Hand washing facilities in accordance with WAC 296-155-17619(5).
NATURE OF OPERATIONS
RENOVATION
WAC 296-155-17625 (2)(b) and (e)

## Slide 18
TRIGGER TASKS IN RENOVATIONS CONSTRUCTION | TRAINING REQUIRED | AIR MONITORING | PERSONAL PROTECTIVE EQUIPMENT | DECONTAMINATION
Objective or Statistical Data: Where the employer has previously monitored for lead exposures, and the data were obtained within the past twelve months during work operations conducted under workplace conditions closely resembling the processes, type of material, control methods, work practices, and environmental conditions used and prevailing in the employer's current operations, the employer may rely on such earlier monitoring results to satisfy the requirements air monitoring if the sampling and analytical methods meet the accuracy required in WAC 296-155-17609. |  |  |  | 
Employee notification. Within five working days after completion of the exposure assessment the employer shall notify each employee in writing of the results which represent that employee's exposure and the employer shall include in the written notice a statement if the employees exposure was at or above that level and a description of the corrective action taken or to be taken to reduce exposure to below that level. |  |  |  | 
NATURE OF OPERATIONS
RENOVATION
WAC 296-155-17625 (2)(b)

## Slide 19
MEDICAL SURVEILLANCE
The purpose of our company’s medical surveillance program is to see if protective equipment and engineering practices are protecting workers. The medical removal program is to protect workers from damaging effects of lead once in their system.
Initial Baseline Blood Lead Level (BLL) (or Zinc Protoporphyrin Levels (ZPP) Test)
Workers will be tested at least every two months for the first six months, and every six months thereafter for employees who are or may be exposed by the employer at or above the action level for more than thirty days in any consecutive twelve months
Follow up every 60 days for workers with a BLL > 40 μg/dL
WAC 296-155-17625 (2)(d), WAC 296-155-17623

## Slide 20
Chelating agents should not routinely be used to remove lead from your bodies and should not be used at all except under the direction of a licensed physician
Workers with elevated blood lead levels above 50 µg/dl temporarily will be “medically removed” from work place. The worker can return when below 40 µg/dl.
MEDICAL SURVEILLANCE
WAC 296-155-17625 (2)(d) and (g), WAC 296-155-17621 (8), WAC 296-155-17623
Elevated BLLs mean low dust work practices and PPE are not being used properly!
Notes: Appendix A to WAC 296-155-176
BLL measurements show the amount of lead circulating in your blood stream, but do not give any information about the amount of lead stored in your various tissues. BLL measurements merely show current absorption of lead, not the effect that lead is having on your body or the effects that past lead exposure may have already caused. Past research into lead-related diseases, however, has focused heavily on associations between BLLs and various diseases. As a result, your BLL is an important indicator of the likelihood that you will gradually acquire a lead-related health impairment or disease.
Once your blood lead level climbs above 40 µg/dl, your risk of disease increases. There is a wide variability of individual response to lead, thus it is difficult to say that a particular BLL in a given person will cause a particular effect. Studies have associated fatal encephalopathy with BLLs as low as 150 µg/dl. Other studies have shown other forms of diseases in some workers with BLLs well below 80 µg/dl. Your BLL is a crucial indicator of the risks to your health, but one other factor is also extremely important. This factor is the length of time you have had elevated BLLs. The longer you have an elevated BLL, the greater the risk that large quantities of lead are being gradually stored in your organs and tissues (body burden). The greater your overall body burden, the greater the chances of substantial permanent damage. The best way to prevent all forms of lead-related impairments and diseases—both short term and long term—is to maintain your BLL below 40 µg/dl. The provisions of the standard are designed with this end in mind.
Your employer has prime responsibility to assure that the provisions of the standard are complied with both by the company and by individual workers. You, as a worker, however, also have a responsibility to assist your employer in complying with the standard. You can play a key role in protecting your own health by learning about the lead hazards and their control, learning what the standard requires, following the standard where it governs your own actions, and seeing that your employer complies with provisions governing employee actions.

## Slide 21
ACCIDENT PREVENTION PLAN
Companies working around lead must have an accident prevention and respiratory protection plan
Visit www.nicasafety.com for more information.
WAC 296-155-17625 (2)(d)

## Slide 22
HAZARD COMMUNICATION TRAINING
Hazard Communication Program including the Globally Harmonized System (GHS) of Classification and Labeling of Chemicals for Washington Employers is a separate class offered by NICA.
Visit www.nicasafety.com for more information.
WAC 296-155-17625 (2)(d)

## Slide 23
LEAD COMPLIANCE PLAN
Written Lead Safety Compliance Plan per WAC 296-155-17611 which needs to be updated every 6 months.
WAC 296-155-17625 (2)(f)

## Slide 24
Renovation, Repair and Painting (RRP) of Lead- Based Paint (EPA)
RRP Rule 40 CFR 745
Any firms (including General and Subcontractors) working in pre-1978 homes must be certified and use lead-safe work practices.
Lead-Based Paint Activities WAC 365-230
Must register with the Dept. of Commerce every 5 years to work on pre-1978 homes in WA
Ensure overall compliance with the RRP Rule
Have a Certified Lead Renovator on staff (8 hour training course)
REGULATIONS FOR LEAD RENOVATION - EPA AND DEPT. OF COMMERCE
Notes: RENOVATION, REPAIR AND MAINTENANCE (RRP) OF LEAD BASED PAINT (EPA) - RRP Rule 40 CFR 745 (epa.gov/lead):
Promulgated the Renovation, Repair, and Painting Program Final Rule. On or after April 22, 2010, any firms, including General Contractors and ALL SUBCONTRACTORS, working in pre-1978 homes and child occupied facilities must be certified firms and use lead-safe work practices during renovations involving Lead Based Paint (LBP). Those firms found to be non-compliant may be liable for civil penalties of up to $37,500 for each violation according to the 1972 Toxic Substance Control Act (TSCA).
Department of Commerce LEAD BASED PAINT ACTIVITIES - WAC 396-230 (commerce.wa.gov/lead) Started administrating the Renovation, Repair and Painting program in Washington on March 16, 2011. Maximum fines of $10,000 per violation.
Construction Firms must become a Certified Firm by registering with the Department of Commerce every 5 years to work on Pre-1978 residences or child occupied facilities in Washington State. Firms must:
Ensure overall compliance with the RRP Rule.
Designate Certified Lead Renovator to be certified through an 8 hour training course approved by Department of Commerce (Refresher every 5 years).
Ensure that all renovation personnel are Certified Renovators or have been trained on-the-job by Certified Renovators.
Deliver pre-renovation education of providing the brochure “Renovate Right” in pre-1978 homes and child-occupied facilities to the owners, tenants, and parents of children.
Meet record keeping requirements.
Certified Renovator Responsibilities include:
Perform work and direct lead-safe work practices, including containment, PPE, cleanup and disposal activities that meet the RRP requirements.
Provide on-the-job training to non-certified workers according to task performed. Use Steps to Lead Safe Renovation, Repair, and Painting as a guide.
Keep records for the project, including having a copy of the initial and/or refresher training certificates onsite (refresher training required every 5 years).
Use EPA-recognized test kits to identify lead-based paint.
Be physically present while posting signs, containing work areas, and cleaning work areas. Be available by phone at other times.
Implement the cleaning verification procedure.

## Slide 25
REGULATIONS FOR LEAD RENOVATION - HUD
Lead-Based Activities in Federally Funded or Assisted Housing are under the LEAD SAFE HOUSING RULE (LSHR):
  24 CFR Part 35, Subparts B through M:
    Dept of Commerce administrates the Federal Department of Housing and Urban Development (HUD) Lead Safe Housing Rule
    LSHR Renovation work can be done by Certified Firms with Certified Renovators
    LSHR Abatement Projects must be done by LEAD Contractor certified firms with Lead Supervisors and Lead Workers only
Notes: LEAD BASED ACTIVITIES IN FEDERALLY FUNDED OR ASSISTED HOUSING - 24 CFR Part 35, Subparts B through M:
The Department of Commerce administrates the Federal Department of Housing and Urban Development (HUD) Lead Safe Housing Rule for renovation in Federally funded or assisted housing (Section 8).
LSHR Renovation work can be done by Certified Firms with Certified Renovators who are also hold a Supervisor Card and non certified but trained workers. LSHR Abatement Projects must be done by LEAD Contractor certified firms with Lead Supervisors and Lead Workers only.
As compared to the RRP, LSHR projects include smaller exclusion levels (2 sq2 interior 20 sq2 exterior), additional prohibited practices (dry scraping, heat guns that char, and use of volatile strippers in enclosed space), specialized cleaning, clearance testing by a Risk Assessor or Inspector, and owners and tenants notification of the presence of lead within 15 days (instead of 30).

## Slide 26
Abatement:
  Abatement means any measure or set of measures specifically designed to permanently eliminate lead-based paint hazards including:
        permanent enclosure or encapsulation
        replacement of lead-painted surfaces
        the removal or covering of lead-contaminated soil
REGULATIONS FOR LEAD ABATEMENT - DEPT OF COMMERCE
Notes: LEAD BASED PAINT ACTIVITIES* - WAC 365-230 (commerce.wa.gov/lead)
Abatement means any measure or set of measures specifically designed to permanently eliminate lead-based paint hazards including: the permanent enclosure or encapsulation of lead-based paint, the replacement of lead-painted surfaces or fixtures, and the removal or covering of lead-contaminated soil. Worker Safety rules for these projects are covered under WAC 296-155-176.

## Slide 27
Abatement Projects require:
  Notification to Commerce for Projects over $25,000
  Registration as a Certified Firm with the Department of Commerce
  Inspector
  Risk Assessor
  Supervisor
  Worker
REGULATIONS FOR LEAD ABATEMENT - DEPT OF COMMERCE
Notes: LEAD ABATEMENT PROJECTS REQUIRE:
Notification to Commerce for Projects over $25,000
Construction Firms must be Registered as a Certified Firm with the WA Department of Commerce
Inspector (3 Day Required, Yearly Refresher): Can perform inspections and clearance testing.
Risk Assessor (5 Day Required Class, Yearly Refresher): Can perform inspections, clearance testing, lead hazard screens and risk assessments.
Supervisor (4 Day Required Class, Yearly Refresher): Performs supervision of abatement projects, preparation of occupant protection plans, abatement reports, and all abatement activities performed by abatement workers.
Worker (2 Day Required Class, Yearly Refresher): Performs abatement activities under the direction of a certified abatement supervisor.

## Slide 28
TESTING FOR LEAD
Required Tests for Pre-1978 Homes:
  You must check for Lead Based Paint using and EPA approved process or assume Lead Based Paint is present
  Give results to owners within 30 days of the completion of the project
Notes: LABOR AND INDUSTRIES TESTING REQUIREMENT FOR WORKER SAFETY
Each employer who has a workplace or operation covered by this standard shall initially determine if any employee may be exposed to lead at or above the action level.
The first step to that is determining if lead is on the job site. A qualified lead Risk Inspector or Assessor may be used or a Certified Renovator may determine if Lead Based Paint is on the project.
REQUIRED TESTS FOR PRE-1978 HOMES:
You must check for Lead Based Paint using an EPA approved process or assume Lead Based Paint is Present
Give results to owners along with project file within 30 days of the completion of the project.
EPA Approved Lead Test Kits
LeadCheck®
LeadCheck® lead test kit can reliably determine that regulated lead- based paint is not present on wood or ferrous metal (alloys that contain iron). This kit is not recognized for use on plaster and drywall.
D-Lead®
Paint Test Kit manufactured by ESCA Tech, Inc., can reliably determine that regulated lead-based paint is not present on wood ferrous metal (alloys that contain iron), drywall and plaster surfaces.
Paint Chip Sampling
Using an EPA approved process and an NLLP lab, a certified renovator may collect paint chips and send for results.
Procedure for Testing
Test in 3 places in each room you want to rule out Lead.
Document findings.You can always assume lead and document your assumption.
Give results to owners along with project file within 30 days of the completion of the project.

## Slide 29
TESTING FOR LEAD
EPA Approved Lead Test Kits and Procedure:
LeadCheck®
D-Lead®
Paint Chip Sampling
Test in 3 places for each room you want to rule out Lead and document your findings
Notes: LABOR AND INDUSTRIES TESTING REQUIREMENT FOR WORKER SAFETY
Each employer who has a workplace or operation covered by this standard shall initially determine if any employee may be exposed to lead at or above the action level.
The first step to that is determining if lead is on the job site. A qualified lead Risk Inspector or Assessor may be used or a Certified Renovator may determine if Lead Based Paint is on the project.
REQUIRED TESTS FOR PRE-1978 HOMES:
You must check for Lead Based Paint using an EPA approved process or assume Lead Based Paint is Present
Give results to owners along with project file within 30 days of the completion of the project.
EPA Approved Lead Test Kits
LeadCheck®
LeadCheck® lead test kit can reliably determine that regulated lead- based paint is not present on wood or ferrous metal (alloys that contain iron). This kit is not recognized for use on plaster and drywall.
D-Lead®
Paint Test Kit manufactured by ESCA Tech, Inc., can reliably determine that regulated lead-based paint is not present on wood ferrous metal (alloys that contain iron), drywall and plaster surfaces.
Paint Chip Sampling
Using an EPA approved process and an NLLP lab, a certified renovator may collect paint chips and send for results.
Procedure for Testing
Test in 3 places in each room you want to rule out Lead.
Document findings.You can always assume lead and document your assumption.
Give results to owners along with project file within 30 days of the completion of the project.

## Slide 30
LEAD EDUCATION
The RRP Pre-Renovation Education Rule:
  Requires Renovation Firms to provide the Renovate Right pamphlet to owner/residents prior to renovation activities in pre-1978 housing and child-occupied facilities
  Specifies requirements for educating residents/occupants and delivering the Renovate Right pamphlet that vary by type of property and the area being renovated
Notes: Under the RRP Rule, Certified Firms MUST:
Give homeowners/residents and child-occupied facility owners/adult representatives copies of the Renovate Right pamphlet.
Let parents/guardians of children using a child-occupied facility know about the renovation and how to get a copy of the Renovate Right pamphlet.
Get confirmation of receipt of the Renovate Right pamphlet from owners, or evidence that the pamphlet was delivered to tenants/residents.
Keep all records for at least 3 years.
In Target Housing – Individual units: Must acquire either written proof of receipt by an adult occupant or proof of delivery/unsuccessful delivery of Renovate Right, or:
Written proof of receipt of Renovate Right by owner or proof of mailing (if mailing, send 7 days prior to renovation).
In Target Housing - Common Areas (Two Options):
Provide written notification to each affected unit and make Renovate Right pamphlet available on request;
Keep copies or pictures of the signs and notices posted.
In Child-Occupied Facilities
Written proof of receipt of Renovate Right by owner or proof of mailing required
(If mailing, send between 60 and 7 days prior to renovation).
Maintain proof of receipt by owner or adult representative, or certify in writing that the Renovate Right pamphlet has been delivered to facility.
Keep copies or pictures of the signs and notices posted in project file.
To Order EPA’s Renovate Right http://bookstore.gpo.gov /

## Slide 31
RENOVATION, REPAIR, PAINTING
Summary:
  All Firms who work in pre-1978 housing and child-occupied facilities must be certified with WA DEPT OF COMMERCE
    Whether or not there is lead
    All subcontractors
  Work must be supervised by a Certified Renovator (8 Hour Class)
    All workers must have non-certified worker training documented
Notes: Under the RRP Rule, Certified Firms MUST:
Give homeowners/residents and child-occupied facility owners/adult representatives copies of the Renovate Right pamphlet.
Let parents/guardians of children using a child-occupied facility know about the renovation and how to get a copy of the Renovate Right pamphlet.
Get confirmation of receipt of the Renovate Right pamphlet from owners, or evidence that the pamphlet was delivered to tenants/residents.
Keep all records for at least 3 years.
In Target Housing – Individual units: Must acquire either written proof of receipt by an adult occupant or proof of delivery/unsuccessful delivery of Renovate Right, or:
Written proof of receipt of Renovate Right by owner or proof of mailing (if mailing, send 7 days prior to renovation).
In Target Housing - Common Areas (Two Options):
Provide written notification to each affected unit and make Renovate Right pamphlet available on request;
Keep copies or pictures of the signs and notices posted.
In Child-Occupied Facilities
Written proof of receipt of Renovate Right by owner or proof of mailing required
(If mailing, send between 60 and 7 days prior to renovation).
Maintain proof of receipt by owner or adult representative, or certify in writing that the Renovate Right pamphlet has been delivered to facility.
Keep copies or pictures of the signs and notices posted in project file.
To Order EPA’s Renovate Right http://bookstore.gpo.gov /

## Slide 32
REGULATIONS: SILICA / MOLD

## Slide 33
AGENCIES REGULATING SILICA/MOLD
OSHA (D.O.L)
WORKER SAFETY
LABOR AND INDUSTRIES
DEPARTMENT OF SAFETY AND HEALTH (DOSH)
FEDERAL DEPARTMENTS
WASHINGTON STATE ENFORCEMENT
AIRBORNE CONTAMINANTS
WAC 296-841

## Slide 34
SILICA / MOLD REGULATIONS
Airborne Contaminants Rule
WAC 296-841 requires sampling for exposures when your employees are potentially exposed above the PEL. Monitoring must be continued until the employer can demonstrate that exposures are no longer at or above the action level.
Proposed OSHA Silica Rules
OSHA is reviewing the construction and general industry PELs for silica in its ongoing silica rule making. The new proposed rule by OSHA is 50 μg/m3. for all industries and types of silica. It will also include an ‘action level’ of 25 μg/m3 that requires employers to institute protective measures. Labor and Industries will be required to adopt the new levels if passed by OSHA.

## Slide 35
RECORD KEEPING

## Slide 36
RECORD KEEPING L&I
The employee's right of access to records
The employer shall make readily available to all affected employees a copy of this standard and its appendices
The employer shall provide, upon request, all materials relating to the employee information and training program to affected employees and their designated representatives, and to L&I
WAC 296-155-17625 (2)(h), WAC 296-155-17629

## Slide 37
RECORD KEEPING L&I
Labor and Industries (WAC 296-155-17629) requires employers with employees that work above the action level of Lead to:
Establish and maintain an accurate record of all monitoring and other data used in conducting employee exposure assessments as required in WAC 296-155-17609.
Establish and maintain an accurate record for each employee subject to medical surveillance as required by WAC 296-155-17621.
Establish and maintain an accurate record for each employee removed from current exposure to lead pursuant to WAC 296-155-17623.
Notes: Contractors with employees that work around any lead containing materials must keep copies of the following for employment plus a duration of 30 years:
Contractors Completed Lead Safety Plan
Respiratory Protection Program
Medical Surveillance for Employees
Fit Test Records
Hazard Communication Program
Monitoring Data

## Slide 38
RECORD KEEPING EPA/DEPT OF COMMERCE
EPA/Department of Commerce requires the following records be available at the work site:
Certified Renovator Certificate
Certified Firm Certificate (EPA and/or WA Dept of Commerce)
Non-Certified Worker Training Documentation

## Slide 39
RECORDKEEPING FOR CERTIFIED FIRMS
Certified Firms must retain all project records for at least 3 years after completion of the renovation, including:
Certified Renovator Certificate
Certified Firm Certificate
Record Keeping Checklist
Pre-Renovation Notification Documentation
Lead Test Results
Non-Certified Worker Training Documentation
Dust Clearance Examination if done by a third party
Photo documentation of practices (optional)
A copy of the project records must be given to the owner within 30 days of the completion of the job.

## Slide 40
RECORDKEEPING FOR CONTRACTORS
Contractors with employees that work around any lead containing materials must keep copies of the following for length of employment plus a duration of 30 years:
Contractors Completed Lead Safety Plan
Respiratory Protection Program
Medical Surveillance for Employees
Fit Test Records
Hazard Communication Program
Monitoring Data

## Slide 41
ASBESTOS ABATEMENT RECORDKEEPING
Certified Asbestos Abatement Contractors must have the following records available at the work site:
Contractor’s Registration
Asbestos Contractor Certification
Asbestos Supervisor Cards
Asbestos Worker or Specialty Training Card
Respirator Fit Test Card
Contractors with employees that work around any asbestos containing materials must keep copies of the following for 30 years:
Medical Surveillance for Employees
Respiratory Protection Program
Fit Test Records
Hazard Communication Program
Monitoring Data

## Slide 42
YOU CAN DO THIS

## Slide 43
CONSISTENT IS EFFICIENT
Follow the regulations and best practices even when not required to build a culture of safety. It’s more cost effective, efficient, and professional.
Having the training, equipment, and PPE will enable your company to cost effectively deal with health hazards.
Notes: Follow the regulations and best practices even when not required to build a culture of safety. It’s more cost effective, efficient, and professional. The logistics, equipment, and training costs of these regulations must be built into any plan that includes renovations.

## Slide 44
CONTAINMENT
PERSONAL PROTECTIVE EQUIPMENT
LOW DUST WORK PRACTICES
DECONTAMINATION
PROTECT WORKERS!
FOUR PRINCIPALS OF PROTECTION

## Slide 45
LNI.WA.GOV
COMMERCE.WA.GOV
EPA.GOV
ECY.WA.GOV - (LOCAL CLEAN AIR)
HUD.GOV
NICASAFETY.COM
RESOURCES

## Slide 46
Funding and support for this project provided by State of Washington, Department of Labor and Industries, Safety and Health Investments projects.