## Slide 1
LEAD, ASBESTOS, SILICA, & MOLD
PART 3
Funding and support for this project provided by State of Washington, Department of Labor and Industries, Safety and Health Investments projects.
HEALTH HAZARDS
IN CONSTRUCTION

## Slide 2
CONTAINMENT

## Slide 3
LEAD/SILICA CONTAINMENT
Containment:
  a system of temporary barriers used to isolate a work area
  keeps dust or debris from escaping while the renovation is being done
  the goal is to make sure the dust doesn’t leave the work area
Notes: THESE ARE REQUIRED PRACTICES LEAD CONTAINMENT PRACTICES PER THE DEPARTMENT OF COMMERCE RRP RULE
THESE ARE RECOMMENDED BEST PRACTICES FOR CONTAINMENT UNDER THE OSHA PROPOSED SILICA STANDARD
CONTAINMENT
“Containment” is a system of temporary barriers used to isolate a work area so that no dust or debris escapes while the renovation is being performed.
Containment is not about “putting up plastic” but rather making sure dust doesn’t leave the work area. Expect fines or cross contamination if dust escapes containment.
Benefits of containment:
Protects residents and workers.
Prevents spread of dust to rest of house/building or neighboring properties.
Makes for an easier cleaning at the end of the job.
SPECIAL CONSIDERATIONS:
Large jobs may require special considerations to get the job done, like:
Power sanders, grinders, and planers, needle guns, and abrasive and sand blasters, each with required HEPA filtered capture attachments.
Use pneumatic and battery powered when possible tools to protect against shock hazards.

## Slide 4
LEAD/SILICA CONTAINMENT
Benefits of Containment:
Protects residents and workers
Prevents the spread of dust to the rest of the house building or neighborhood
Makes clean-up at the end of the job easier
Notes: THESE ARE REQUIRED PRACTICES LEAD CONTAINMENT PRACTICES PER THE DEPARTMENT OF COMMERCE RRP RULE
THESE ARE RECOMMENDED BEST PRACTICES FOR CONTAINMENT UNDER THE OSHA PROPOSED SILICA STANDARD
CONTAINMENT
“Containment” is a system of temporary barriers used to isolate a work area so that no dust or debris escapes while the renovation is being performed.
Containment is not about “putting up plastic” but rather making sure dust doesn’t leave the work area. Expect fines or cross contamination if dust escapes containment.
Benefits of containment:
Protects residents and workers.
Prevents spread of dust to rest of house/building or neighboring properties.
Makes for an easier cleaning at the end of the job.
SPECIAL CONSIDERATIONS:
Large jobs may require special considerations to get the job done, like:
Power sanders, grinders, and planers, needle guns, and abrasive and sand blasters, each with required HEPA filtered capture attachments.
Use pneumatic and battery powered when possible tools to protect against shock hazards.

## Slide 5
WAC 296-155-17627 (11)
LEAD/SILICA INTERIOR
Post Warning Signs
Create double layer plastic entry door
Use minimum 6’ plastic in each direction horizontal
Vertical containment can be used
Cover doors, windows, HVAC vents
Cover unmovable objects

## Slide 6
LEAD/SILICA EXTERIOR
Post Warning Signs
Setup 20’ limited access zone
Use minimum 10’ plastic in each direction horizontal
Vertical containment can be used (must be if less than 10’)
Cover doors, windows, HVAC vents
Cover unmovable objects
Notes: Lead Safe Work Practices Required
when you disturb more than 6’ sq. of interior or 20’ of exterior, or window replacement or demolition

## Slide 7
ASBESTOS/MOLD CONTAINMENT
Required Practices for Asbestos Class I or II Work:
  Must be done by Certified Asbestos Contractors only
  Containment must be built to control the fibers released during a renovation
Recommended Practices for Mold Remediation Work in Condition II or III:
  Workers can be protected in areas where wet indoor mold growing conditions exist or visible mold showing by following the same containment and air control practices as the asbestos standard requires
Negative Air Machines:
  Must be used in containment to direct the flow of asbestos fibers or wold spores out of the work area through HEPA filter
Notes: REQUIRED PRACTICES FOR ASBESTOS CLASS I or II WORK MUST BE DONE BY CERTIFIED ASBESTOS CONTRACTORS ONLY
Containment must be built to control the fibers released during a renovation. WAC 296-62-07712 has the minimum work practices and containment requirements for asbestos projects .
RECOMMENDED PRACTICES FOR MOLD REMEDIATION WORK IN CONDITION II or III Workers can be protected in areas where wet indoor mold growing conditions exist or visible mold showing by following the same containment and air control practices as the asbestos standard requires.
NEGATIVE AIR MACHINES
A negative air machine must be used in containment to direct the flow of asbestos fibers or mold spores out of the work area through the negative air machine’s HEPA filter and directed to a safe location (must run 24 hours/day during project).
The system is tested by visually observing smoke released into the containment flowing into the machine.
It then needs to maintain -0.02 column inches of water pressure differential, relative to outside pressure.
At least 4 air changes per hour must be maintained in the work area.
The formula for calculating negative air machines needed is: LxWxH/15 / CFM of Units Needed
Enough air machines must be setup to maintain the pressure differential and air changes per hour required.
A manometer measures the pressure differential in the containment and surrounding areas.

## Slide 8
PLAY CONTAINMENT VIDEO

## Slide 9
MONITORING
AND PPE

## Slide 10
AIR MONITORING
Air Monitoring:
  Labor and Industries requires air monitoring for Airborne Contaminates when work activities have the potential to exceed the action level, which is lower than the PEL
              e.g: lead’s action level is 30 µg/m3
  is an ‘exposure assessment’ and determine the actual exposure to an employee if they don’t wear a respirator and helps determine proper respiratory protection.
Personal Monitoring Pump
WAC 296-155-17609 (2)
Notes: AIR MONITORING
Labor and Industries requires air monitoring for Airborne Contaminants (WAC 296-841)when the work activities have the potential to exceed the action level of, for these health hazards (other materials are also regulated):
Lead 30 μg/m3
Asbestos .1/ffcc
Silica 25 μg/m3 (proposed)
The purpose is to an ‘exposure assessment’ and determine the actual exposure to an employee if they were not wearing a respirator. It’s also a good indication of the effectiveness of the low dust work practices a company is using and weather they are working or need to be modified.
Personal air monitoring must be done for each work process or on a suggested 25% of workers in an area.
Area monitoring is also required for some contaminants and requires a separate pump and monitoring media.
Worker wears a personal air monitoring pump with a hose to their breathing zone, the space around and in front of an employee's nose and mouth, forming a hemisphere with a six to nine inch radius. Personal air samples should be taken that represent an employee's usual or worst-case exposure during the entire shift. Results are then sent to a lab and workers are notified within 5 days of the results of their exposure level for each type of contaminant.
While monitoring, you have to protect your employees for contaminants. As a best practice, choosing a full face respirator over a half mask during the exposure monitoring will protect them to up to 50x the PEL.

## Slide 11
AIR MONITORING
Permissible Exposure Limits (PEL):
  PELs are the measured amount of a substance you can be exposed to over an 8 hour time weighted average (TWA) without wearing a respirator
- Lead = 50 μg/m3 8 hr/TWA
- Asbestos = .1 fiber/cc TWA - 1 fiber/cc STEL
- Silica (crystalline quartz) = .01 mg/m3 8 hr/TWA
Mold = Higher Outside Spore count than Inside (best practice)
  If exposure to a worker exceeds the PEL, they must wear a respirator in addition to engineering controls
WAC 296-155-17631 (13)

## Slide 12
Monitoring Basics:
The same sampling pump can be used for each type of containment, but the cassette that collects the information is different
Worker wears a personal air monitoring pump with a hose to their breathing zone
AIR MONITOR

## Slide 13
AIR MONITORING
Sampling media for each hazard is different:
                Asbestos: 25mm Asbestos PCM Cassette
                Lead: 37mm 3pc Cassette w/ 0.8um MCE
                Cyclone and holder for 37mm Cassettes
                Silica: 37mm 3pc 5.0um PVC Preweighted
                Cyclone and holder for 37mm Cassettes
                Mold: Air-O-Cell Cassette

## Slide 14
RESPIRATORS
Respirators are needed when:
  Chemical “Permissible Exposure Limits” (PELs) for chemicals are exceeded
  Dust, mists, gases, vapors or fumes could cause damage to your lungs
  Air purifying respirators work to filter the air in the room before it enters your lungs
Notes: To work properly, respirators need to filter the air before you breath it. Each respirator needs a P100 or HEPA filter attachment to be 99.97% efficient to .3 micro to protect workers.

## Slide 15
PERSONAL PROTECTIVE EQUIPMENT
Respirators have an Assigned Protection Factor (APF):
  Protects workers a multiplier of the PEL they are exposed to
  This is a simplified chart of the APFs for respirators for Asbestos, Lead, Silica, or Mold:
Up to 10x the PEL | Half Face Respirator
Up to 50x the PEL | Full Face Respirator
Up to 1000x the PEL | Supplied Air Full-facepiece and designed to operate in pressure-demand or other positive-pressure mode
Up to 1000x the PEL | Powered Air Purifying Respirator
Notes: To work properly, respirators need to filter the air before you breath it. Each respirator needs a P100 or HEPA filter attachment to be 99.97% efficient to .3 micro to protect workers.

## Slide 16
Note: Powered Air Purifying Respirators can be worn with a beard and do not require fit-testing
PAPR

## Slide 17
Filters work by air moving through a series of microscopic mesh that traps particulates bigger than the holes in the mesh
P95 = 95% efficient to .3 micron
P100 = 99.97% efficient to .3
Each Respirator needs a P100 or HEPA filter when dealing with most health hazards
Change filters regularly to protect workers.
FILTERS
New filter
Used filter

## Slide 18
Filters only work on particulates!
Other hazards from gases or vapors from the products you are using could be present.
Consult your SDS sheets all on products to make sure you do not need specific vapor Cartridges in addition to filters.
Half mask and Full Face Respirators DO NOT WORK IN OXYGEN DEFICIENT ATOMSPHERES!
WARNING!

## Slide 19
PERSONAL PROTECTIVE EQUIPMENT
Recommended PPE for Lead, Silica, Asbestos Class II, III, IV (and Best Practice for Mold Remediation):
  Goggles
  Respirator with P100 filter
      half mask with goggles or full face mask is based on exposure monitoring and trigger tasks performed
  Coveralls
  Gloves
  Disposable Foot Covers
WAC 296-155-17613 (4) WAC 296-155-17615 (5)

## Slide 20
PERSONAL PROTECTIVE EQUIPMENT
For Certified Asbestos Contractors Only - Required PPE for Asbestos Class I Work:
  A full facepiece supplied-air respirator operated in the pressure demand mode equipped with either an auxiliary positive pressure self-contained breathing apparatus or a HEPA filter egress cartridge, to employees engaged in the following asbestos operations:
  (i) Inside negative pressure enclosures used
  (ii) Any dry removal of asbestos. doing dry removal,
Alternate Respirators could be used IF:
  If they are not dealing with friable asbestos inside a negative pressure enclosure, they go by the APF.
  If they have an NEA, they could actually wear a half mask with a P100 filter
  working on thermal system insulation (TSI) inside a negative pressure enclosure, it is excluded from the pressure demand requirements
  If they use continuous flow, they cannot exceed 1f/cc
Notes: FOR CERTIFIED ASBESTOS CONTRACTORS ONLY: REQUIRED PPE FOR ASBESTOS CLASS I WORK
(3) Respirator selection. The employer must:
(a) Select and provide to employees appropriate respirators as specified in this section, and in WAC 296-842-13005, in the respirator rule.
Make sure filtering facepiece respirators are not selected or used for protection against asbestos fibers.
(b) Provide employees with an air-purifying, half-facepiece respirator, other than a filtering-facepiece respirator, that is equipped with a HEPA filter or an N-, R-, or P-100 series filter whenever the employee performs:
(i) Class II and III asbestos work for which no negative-exposure assessment is available;
(ii) Class III asbestos work involving disturbances of TSI or surfacing ACM or PACM.
(c) Equip any powered air-purifying respirator (PAPR) or negative pressure air-purifying respirator with HEPA filters or N-, R-, or P-100 series filters.
(4) Special respiratory protection requirements.
(a) Unless specifically identified in this subsection, respirator selection for asbestos removal, demolition, and renovation operations shall be in accordance with the selection specifications of this section and the general selection requirements in WAC 296-842-13005, found in the respirator rule. The employer must provide and require to be worn, at no cost to the employee, a full facepiece supplied-air respirator operated in the pressure demand mode equipped with either an auxiliary positive pressure self-contained breathing apparatus or a HEPA filter egress cartridge, to employees engaged in the following asbestos operations:
(i) Inside negative pressure enclosures used for removal, demolition, and renovation of friable asbestos from walls, ceilings, vessels, ventilation ducts, elevator shafts, and other structural members, but does not include pipes or piping systems; or
(ii) Any dry removal of asbestos.
(b) For all Class I work excluded or not specified in (a)(i) and (ii) of this subsection, when a negative-exposure assessment is not available, and the exposure assessment indicates the exposure level will be at or below 1 f/cc as an 8-hour time weighted average, employers must provide employees with one of the following respirators:
(i) A tight-fitting, powered, air-purifying respirator equipped with high-efficiency filters;
(ii) A full-facepiece supplied-air respirator operated in the pressure-demand mode equipped with either HEPA egress cartridges; or
(iii) An auxiliary positive-pressure, self-contained breathing apparatus.
(c) Whenever the employees are in a regulated area performing Class I asbestos work for which a negative exposure assessment is not available, and an exposure assessment indicates that the exposure level will be above 1 f/cc as an 8-hour TWA, employers must provide a full facepiece supplied-air respirator operated in the pressure-demand mode equipped with an auxiliary positive-pressure self-contained breathing apparatus.
EXCEPTION:
In lieu of the supplied-air respirator required by subsection (4) of this section, an employer may provide and require to be worn, at no cost to the employee, a full facepiece supplied-air respirator operated in the continuous flow mode equipped with either an auxiliary positive pressure self-contained breathing apparatus or a back-up HEPA filter egress cartridge where daily and historical personal monitoring data indicates the concentration of asbestos fibers is not reasonably expected to exceed 10 f/cc. The continuous flow respirator shall be operated at a minimum air flow rate of six cubic feet per minute at the facepiece using respirable air supplied as required by chapter 296-842 WAC, Respirators.
(5) Respirator fit testing.
(a) For each employee wearing negative pressure respirators, employers shall perform either quantitative or qualitative face fit tests at the time of initial fitting and at least annually thereafter. The qualitative fit tests may be used only for testing the fit of half-mask respirators where they are permitted to be worn.
(b) Any supplied-air respirator facepiece equipped with a back-up HEPA filter egress cartridge shall be quantitatively fit tested (see WAC 296-62-07160 through 296-62-07162 and 296-62-07201 through 296-62-07248).

## Slide 21
RESPIRATORY PROTECTION PROGRAM
Respiratory Protection Program:
All companies that require or allow their employees to wear respirators must have a written respiratory protection plan that covers:
  Respirator Selection
  Training
  Medical Evaluations
  Fit Testing
  Respirator Storage, Cleaning, Maintenance & Repair
  Respirator Program Evaluation
  Record Keeping

## Slide 22
PLAY AIR MONITORING AND
PPE VIDEO

## Slide 23
WORK PRACTICES

## Slide 24
Chart: Traditional Work Practices
| Hand Sanding | Power Sanding | Interior Demolition
Series1 | 254 | 571 | 108
*
LEAD DUST GENERATED
Permissible Exposure Limit (PEL) Lead = 50 µg/m3
Notes: This chart shows the amount of lead generated while doing these different work practices. Both hand sanding and interior demolition are under 10x the PEL and you could use a half mask respirator for protection. However power sanding would require a full face respirator. Instead of recommending different levels of minimum protection - EPA prohibits power sanding without a HEPA vacuum attachment.

## Slide 25
PROHIBITED PRACTICES RRP
Work Practices to Protect Workers:
The dust created for renovations where lead-based paint, asbestos containing materials, silica, or mold spores are present can generally be reduced by following certain required and best practices.
NOT ONLY DO THESE PRACTICES RAISE THE PARTICULATES WORKERS ARE EXPOSED TO …. THEY ARE PROHIBITED PRACTICES UNDER RRP FOR WORK WITH LEAD BASED PAINT:
Open flame or torch burning LBP
2) Power sanding or grinding without HEPA vacuum attachment
3) Using a Heat Gun at over 1100 degrees
PROHIBITED PRACTICES UNDER LSHR FOR WORK WITH LEAD BASED PAINT:
Heat guns that char
2) Dry scraping
3) Use of a volatile stripper in an enclosed space

## Slide 26
LOW DUST WORK PRACTICES
Interior:
  Use additional containment at the source of the dust when possible
  Keep materials intact or in as large of piece as possible
  Use wet methods during demolition, scraping and heat gun applications
  Use innovative methods to control dust while drilling

## Slide 27
LOW DUST WORK PRACTICES
Interior:
Use power tools with HEPA dust collection systems
  Using NIOSH approved 99.97% HEPA Vacuums
        Vacuums need to be maintained to stay in compliance
        HEPA vacuum required to comply with RRP and Asbestos regulations
Clean up debris throughout the day

## Slide 28
LOW DUST WORK PRACTICES
Exterior:
  Water has to be filtered and contained while pressure washing the outside of a building with lead paint
        Direct water flow through a filter and capture all dusts and chips
        Remaining water is captured and pumped into the public sewer system through a toilet
WAC 296-155-17615 (5)

## Slide 29
L&I REQUIRED HOUSEKEEPING
All surfaces shall be maintained as free as practicable of accumulations of lead.
Clean-up of floors and other surfaces where lead accumulates shall wherever possible
Shoveling, dry or wet sweeping, and brushing may be used only where vacuuming or other equally effective methods have been tried and found not to be effective.
Use HEPA vacuums and maintain them properly.
Compressed air shall not be used to remove lead from any surface.
WAC 296-155-17617
Notes: Interior Cleaning Requirements:
All surfaces shall be maintained as free as practicable of accumulations of lead.
Collect all paint chips, debris, dust and seal in heavy duty plastic bags.
Shoveling, dry or wet sweeping, and brushing may be used only where vacuuming or other equally effective methods have been tried and found not to be effective.
Mist, remove, fold (dirty side in) and tape or seal protective sheeting. Dispose of sheeting as waste.
Plastic sheeting between non-contaminated rooms and work areas must remain in place until after cleaning and removal of other sheeting.
HEPA vacuum or wet wipe walls from high to low, then HEPA vacuum remaining surfaces and wipe with a damp cloth.
HEPA vacuums shall be used and emptied in a manner which minimizes the reentry of lead into the workplace
Clean 2 feet beyond the contained work area. Use disposable wipes.
For carpet or rug, use HEPA vacuum with beater bar.
HEPA vacuum and wet mop uncarpeted floors -two-bucket mopping method or wet mopping system.

## Slide 30
RRP CLEANING ACTIVITIES
Interior Cleaning Requirements:
  All surfaces should be free as practicable of accumulations of lead
  Collect all paint chips, debris, dust and seal in heavy duty plastic bags
  Shoveling, dry or wet sweeping and brushing may be sued only where vacuuming is found not effective
  Mist, remove, fold (dirty side in) and tape protective sheeting and dispose as waste
  Plastic used as containment must remain in place until after cleaning
  HEPA vacuum or wet wipe walls from high to low and surfaces then empty vacuum to minimize reentry of lead
Notes: Interior Cleaning Requirements:
All surfaces shall be maintained as free as practicable of accumulations of lead.
Collect all paint chips, debris, dust and seal in heavy duty plastic bags.
Shoveling, dry or wet sweeping, and brushing may be used only where vacuuming or other equally effective methods have been tried and found not to be effective.
Mist, remove, fold (dirty side in) and tape or seal protective sheeting. Dispose of sheeting as waste.
Plastic sheeting between non-contaminated rooms and work areas must remain in place until after cleaning and removal of other sheeting.
HEPA vacuum or wet wipe walls from high to low, then HEPA vacuum remaining surfaces and wipe with a damp cloth.
HEPA vacuums shall be used and emptied in a manner which minimizes the reentry of lead into the workplace
Clean 2 feet beyond the contained work area. Use disposable wipes.
For carpet or rug, use HEPA vacuum with beater bar.
HEPA vacuum and wet mop uncarpeted floors -two-bucket mopping method or wet mopping system.

## Slide 31
RRP CLEANING ACTIVITIES
Visible Inspection:
  Conducted by Certified Renovator and a Competent Person
  Put on disposable foot covers before entering the work area
  Make sure there is adequate lighting in the work area
  Turn on all of the lights or use a bright, white-light flashlight
  Systematically look for dust and debris on every horizontal surface in the work area and 2 feet beyond
  Work from the farthest area from the entry to the entry
  Closely examine each surface
Notes: Visible Inspection:
Conducted by Certified Renovator and a Competent Person.
Put on disposable foot covers before entering the work area.
Make sure there is adequate lighting in the work area.
Turn-on all of the lights or use a bright, white-light flashlight.
Systematically look for dust and debris on every horizontal surface in the work area and 2 feet beyond.
Work from the farthest area from the entry to the entry.
Closely examine each surface

## Slide 32
CLEANING CLEARANCE - RRP
Cleaning Verification Procedure (RRP) required when project with Lead is Finished:
  Certified Firm finishes a Renovation Project, the Certified Renovator can use a cleaning verification card to do a visual test to “clear” the project.
  Wipe each window sill within the work area
  Use a single wet disposable cleaning cloth per window sill
  Wipe uncarpeted floors and all countertops
  Wipe up to a maximum of 40 sq2 per cloth
  Compare each wipe to the Cleaning Verification card
Notes: When the Lead Project is Finished:
Renovation Projects:
Certified Firm finishes a Renovation project, the Certified Renovator can use a cleaning verification card and do a visual test to ‘clear’ the projects for normal use.
Abatement and LSHR Clearance: Requires a third party Lead Risk Assessor or Inspector to use wipe clearance sampling to ‘clear’ the projects. Dust clearance levels are shown below.
Interior Dust Clearance Levels 40 μg/ft sq - Floors 250 μg/ft sq - Interior sills
400 μg/ft sq - Troughs
EPA Soil Remediation Thresholds:
If soil is tested the following thresholds are used to determine if soil remediation or interim controls are required.
5000 ppm - General Soil 1200 ppm - Building
Perimeter/Yard target housing
400 ppm - Play Areas
WA State Soil Threshold:
250 ppm - All soil
WA Soil interim Control Standard:
Grass, mulch, shrubbery and other landscaping materials are not considered permanent covering, but may be used as interim controls except in:
A child’s play area, or any bare soil area where a child under six years of age regularly plays where soil lead levels exceed 250 ppm.
A garden area, or any other area where bare soils produce edibles intended for human consumption, where soil lead levels exceed 250 ppm.

## Slide 33
RRP CLEANING VERIFICATION
Dust Clearance Examination (RRP/LSHR Rule Only):
  A dust clearance examination may be performed instead of cleaning verification
  Must be conducted by a third party Certified Lead Inspector, Risk Assessor, or Dust Sampling Technician
  Abatement and LSHR Clearance:
  Requires a third party Lead Risk Assessor or Inspector to use wipe clearance sampling to “clear” the project
Notes: Cleaning Verification Procedure (RRP):
Wipe each window sill within the work area.
Use a single wet disposable cleaning cloth per window sill.
Wipe uncarpeted floors and all countertops with wet disposable cleaning cloths.
Wipe up to a maximum of 40 sq2 per cloth.
Compare each wipe to the CV card. If the cloth matches or is lighter than the CV card, the surface has passed cleaning verification and no further action is required.If the cloth is darker than the CV card, re-clean and repeat the CV process.
If the second wet cloth fails, wait 1 hour or until surfaces are dry, and then wipe with an electrostatically charged white disposable cleaning cloth designed to be used for cleaning hard surfaces. This completes the cleaning verification.
Dust Clearance Examination (RRP/LSHR RULE ONLY)
A dust clearance examination may be performed instead of cleaning verification. A clearance examination must be a conducted by a third party Certified Lead Inspector, Risk Assessor, or Dust Sampling Technician.

## Slide 34
RRP CLEANING VERIFICATION
Exterior Cleaning Visual Inspection (RRP):
  Certified Renovator conducts a visual inspection after any cleaning
  Determines if any visible dust and debris are present in and beyond the work area
  If found, collect and dispose of all paint chips, dust and debris
  After re-cleaning, conduct another visual inspection and if all areas pass, warning signs may be removed

## Slide 35
GENERAL CLEANING AND DISPOSAL
Waste handling and disposal:
Place waste in heavy duty plastic bag.
“Gooseneck seal” the bag with duct tape.
Carefully dispose of waste in accordance with Federal and other regulations.
HEPA vacuum the exterior of the waste bag before removing it from the work area.
Store waste in a secure area.
According to Federal law, in housing:
Waste must be disposed of as normal house-hold waste.
In non-residential child-occupied facilities: If waste exceeds 220 lbs, treat all debris as hazardous.
Final Cleaning
Negative Air Machine if used
DECON
WORK AREA
CLEANING PROCEDURES
Gross Removal/Detailing Cleaning
WAC 296-155-17615 (5)

## Slide 36
PLAY WORK PRACTICES VIDEO

## Slide 37
DECON

## Slide 38
FULL 3 STEP DECONTAMINATION
REGULATED AREA (WORK AREA) |  | A I RLOCK | Store/Clean WasteBags | A I RLOCK | Airlock, Ramp or Shoot to Secure Dumpster or enclosed vehicle for regulated waste.
AIRLOCK |  |  |  |  | 
EQUIPMENT ROOM (DIRTY AREA) |  |  |  |  | 
AIRLOCK (OMIT FOR DRY DECON) |  |  |  |  | 
SHOWER (OMIT FOR DRY DECON) |  |  |  |  | 
AIRLOCK (OMIT FOR DRY DECON) |  |  |  |  | 
CHANGE ROOM (CLEAN AREA) |  |  |  |  | 
PUBLIC AREA |  |  | HAND WASHING AVAILABLE (SOAP AND WATER) |  | EATING AREA FREE FROM HEALTH HAZARDS
Showers:
Water temperature for shower must be > 85O.
Water must be pumped through a HEPA filter into a public sewer toilet or approved disposal outlet.
If employer provides shower, they must make sure it is being used by employees on the job site.
Airlocks:
Must inhibit airflow between chambers. Airlocks are generally built with three layers of plastic, the center layer having an opening for workers to pass through. Note: For Lead Renovation projects only two layers of plastic is required under the RRP for entry doors and no specific airflow measurements are required.
CONTAINMENT/DECON SAMPLE
Always wash your hands before eating or drinking after working in a regulated area!
Notes: Note: For Lead in Construction, under the 296-155-17619 standard showers are required where feasible. However, 296-155-17609 lists activities such as manual demolition of structures (e.g, dry wall), manual scraping, manual sanding, heat gun applications, power tool cleaning with dust collection systems; and spray painting with lead paint that do not require shower facilities onsite.

## Slide 39
DECONTAMINATION
Decontamination for Asbestos Contractors:
  When leaving the regulated area, all workers, supervisors and monitors must exit through a decon unit
  A three stage decon unit is generally used:
      Stage 1: Change Room - remove all disposable clothes, clothing, except respirator
      Stage 2: Shower - shower and remove respirator
      Stage 3: Clean room - change into clean clothes and exit containment area

## Slide 40
DECONTAMINATION
Decontamination for Lead, Silica and Mold projects where showers are not feasible or not required:
  Setup a decon area on plastic or in a contained room
  Remove shoe coverings and HEPA vacuum or wipe shoes
  “Dry Decon” yourself using a HEPA vacuum, remove coveralls by rolling down the garment to reduce dust and then vacuum clothes again
WAC 296-155-17615 (5)

## Slide 41
DECONTAMINATION
Decontamination continued:
  After “Dry Decon,” remove gloves if used, and respirator last, then carefully wash hands and face
  Dispose all used clothing the same way as lead waste
  Do not take contaminates home to your family on your clothes or in your car

## Slide 42
PLAY DECON VIDEO

## Slide 43
YOU CAN DO THIS

## Slide 44
CONSISTENT IS EFFICIENT
Follow the regulations and best practices even when not required to build a culture of safety. It’s more cost effective, efficient, and professional.
Having the training, equipment, and PPE will enable your company to cost effectively deal with health hazards.
Notes: Follow the regulations and best practices even when not required to build a culture of safety. It’s more cost effective, efficient, and professional. The logistics, equipment, and training costs of these regulations must be built into any plan that includes renovations.

## Slide 45
CONTAINMENT
PERSONAL PROTECTIVE EQUIPMENT
LOW DUST WORK PRACTICES
DECONTAMINATION
PROTECT WORKERS!
FOUR PRINCIPALS OF PROTECTION

## Slide 46
LNI.WA.GOV
COMMERCE.WA.GOV
EPA.GOV
ECY.WA.GOV - (LOCAL CLEAN AIR)
HUD.GOV
NICASAFETY.COM
RESOURCES

## Slide 47
Funding and support for this project provided by State of Washington, Department of Labor and Industries, Safety and Health Investments projects.